## Slide 1: Global Radio basic Intro (Mixed-Mode)

## Slide 2: Overview
HW/SW Architectural and layer

## Slide 3: Overview
Arch/DB/History
  Radio Architecture
  Database view
  Startup
  Deployment view
TX/RX
  Design WoW
  Tx Module
  Carrier Event Processing
  SPLC
  Rx Module
Debugging/QA
  UT
  QA

## Slide 4: Radio Architecture

## Slide 5: Radio – digital/analog line
DU (Digital Unit)
RU (Radio Unit)
CPRI 2.5G, 5G, 9.8G, or 10.1G
DL
UL
Digital Section
DL
UL
Linearization
DL
Up Convert
DL
PA
Filter Unit
DL
LNA
Down Convert
UL
UL
A
B
C
D
DL
UL
ADC – Analog to Digital Converter DAC – Digital to Analog Converter LNA – Low Noise Amplifier PA – Power Amplifier
DAC
ADC
Digital
Analog
ADC
TOR (PA output)

## Slide 6: Radio – analog

## Slide 7: Legacy view (warp 3x)

## Slide 8: Radio application, middleware and OS
…/radiosw/sw/app
/proj/crbs/radiosw/twh/tools/ose*
/proj/crbs/radiosw/twh/tools/xp
…/radiosw/external
/proj/crbs/radiosw/twh/tools/ricr
…/radiosw/external
/proj/crbs/radiosw/twh/tools
…/radiosw/external

## Slide 9: Digital ASIC evolution
Platform4
Platform5
mRRUS
Platform5.x
IRU
NGR G1
NGR G2
WARP1.7
COLI: warpA warpB
WARP3
COLI: warp3
WARP3.5
COLI: warp3
WARP3.5 x2
COLI: warp:0 warp:1
WARP3.5
COLI: warp:0
iWARP3.5
COLI: warp:0
Xenon
AAS
Xenon
/Radon

## Slide 10: RU legacy naming – 23/1056-HRB 105 600
X | #TX | #RX | Duplex mode
0 | 1 | 2 | FDD
1 | 2 | 2 | FDD
2 | 2 | 4 | FDD
3 | 4 | 4 | FDD
5 | 1 | 2 | TDD
6 | 2 | 2 | TDD
7 | 4 | 4 | TDD
8 | 8 | 8 | TDD
A | 0 | 2 | FDD
C | 0 | 2 | TDD
E | 2 | 0 | FDD
RADIO_NAME XY BZ
RADIO_NAME | Name Expanded
RUG | Radio Unit GSM
RUW | Radio Unit WCDMA
RUL | Radio Unit LTE
RUS | Radio Unit Multi-Standard
RRUG | Remote Radio Unit GSM
RRUW | Remote Radio Unit WCDMA
RRUL | Remote Radio Unit LTE
RRUS | Remote Radio Unit Multi-Standard
AIR | Antenna Integrated Radio
mRRUS | Micro Remote Radio Unit Multi-Standard
Y | RU Platform
1 | 4
2 | 5, 5.2, 5.3
3 | 5 (TK)
Z = Operating Band
0
1
2
3
4
5
6
7
…
33
34
35
36
37
38
39
40
Platform 4
  RUL 01 B13
  RUW 01 B1
  RUS 01 B3
  RRUS 01 B9
  RRUS 11 B5
  RRUS 61 B40B
  RRUS 61 B40C
  AIR 21 B2a B4p
    RRUS 0Z B2
Platform 5
  RUS 02 B2
  RRUS 12 B3
  RRUS 62 B41D
  RRUS E2 B29
mRRUS
  mRRUS 12 B13
Platform 5.2 FDD:
  AIR 32 B4
    RRUS 32A B4
  RRUS 32 B30
Platform 5.3 TDD:
  RRUS 72 B41

## Slide 11: RU new naming (examples) – 23/1056-HRB 105 600
#TX | #RX | Random #
1 | 2 | XX
2 | 2 | XX
2 | 4 | XX
3 | 6 | XX
4 | 4 | XX
4 | 8 | XX
6 | 6 | XX
8 | 8 | XX
0 | 2 | XX
2 | 0 | XX
1 | 2 | XX
RADIO_NAME #Tx#RxXX BZ
RADIO_NAME | Name Expanded
RU | Radio Unit
RRU | Remote Radio Unit
AIR | Antenna Integrated Radio
IRU | Indoor Radio Unit
RD | Radio Dot
Z = Operating Band
0
1
2
3
4
5
6
7
…
33
34
35
36
37
38
39
40
NGR G1
  RRU 2217 B1
  RRU 0208 B1 (2Rx)
  RRU 2203 B1 (mRRUS)
NGR G2
  RRU 2212 B3
  RRU 4415 B7
IRU
  IRU 2242
RD
  RD 2242 B4

## Slide 12: Transmitter
Sync CPRI
Channel
Filter
EQ
Up-sampling
Set frequency
within IBW
Combine
carriers
Clipping
DPD
Digital →
Analog
Up-convert
to RF
Amplify
TXBP
Filter
Duplex:
One antenna
TX & RX
Power control loop
Adaptive Digital
Pre-Distortion loop
x
y
Pre-distortion
function
x
y
PA distortion
PA designed for PAR≤7.5dB
Clipping limits PAR to 7.5dB
High signal PAR
=> Doherty PA for good efficiency
WARP
PA
TX
FU
IBW Instantaneous Band Width
RF Radio Frequency
TXBP Transmitter Band Pass
EQ Equalizer
PAR Peak to Average Ratio
DPD Digital Pre-Distortion

## Slide 13: Receiver
RXBP
Filter
Duplex:
One antenna
TX & RX
Low Noise
Amplifier
Image Rejection
Filter
Down Conv.
Anti-Alias
Filter
Analog→
Digital
Demodulate/
Freq translate
Down Convert
To Base Band
Down-sampling
Channel
Filter
IQ Formatting
Limited dynamic range in ADC
Automatic Gain
Control (AGC)
AGC
Down Conv.
Gain varies in temperature
Gain spread between units
VGA
WARP
FU
RX
RXBP Receiver Band Pass
LNA Low Noise Amplifier
RF Radio Frequency
IF Intermediate Frequency
ADC Analog to Digital Converter
AGC Automatic Gain Control
VGA Variable Gain Amplifier

## Slide 14: Long Long time Ago…
RICR
XPP
External Interfaces for Radio Operation and Management
Configuration, and resource management
Hardware Abstraction layer. Facilitate HW configuration and Supervision
No layer rules enforcement resulting in
Common Functions and Radio Control
Drivers
Operating system & Services

## Slide 15: What is wrong?
Tight coupling of functional blocks
  High dependency between different SW components [e.g. TX & RX]
  Knowledge of Platform and platform variants are spread across many functional block’s and SW components which results in:
    Result complex unit and module testing and integration
    Does not foster parallel development
    Hard to introduce new features [e.g. SPLC]
SW does not easily scale in response to hardware evolution
  Code erosion made it difficult to meet scalability requirement
  RF Branch knowledge is hard coded and spread to many SW functions and blocks
Difficult to Maintain
  Lack of enforced layer architecture and rules contribute to code being introduced in the wrong layer
Carrier related data is copied and manipulated by different functional blocks
  No clear data ownership rules enforced
Rules governing Hal layer isn’t consistent
  Some functional blocks call drivers directly [harder to support new HW]

## Slide 16: Now
Service Control & Services layers
The focus of modularization
Radio Resources management and coordination

## Slide 17: What is New?
Functional encapsulation at each layer
  Loosely coupled Layers
Clear architectural guidelines governing the scope and granularity of the SW layers and components
  Easy to maintain
Clear and well defined interfaces
Clear data ownership rules
Make scaling of the software easier, in response to the Radio HW evolution
  Enforce data driven approach to define the Radio capabilities, Modules cardinality, and the dependencies of the SW modules
    Data Driven means that the values are defined in the database and discovered by the services at startup rather than embedded in the SW.
  Enforce OO design rules and patterns [Encapsulation and inheritance]
  Support Platform 4 and beyond
Facilitate individual module testing independent of the other modules
Allows easier integration of new SW to main track (only need to lock some modules instead of all code during merges)
Notes: 2012-10-19
17
Modularization Overview

## Slide 18: More Detail of Layers
Service Control Layer:
  The Service Control Layer shall contain the Service Controllers which are responsible to implement and orchestrate logic and events that can be associated with certain functionality. An example of such functionality is Carrier handling, which deals with the allocation and control of radio resources needed to implement a radio carrier.
  Service Controllers should have no HW related dependencies or knowledge
Service Layer:
  The Service layer shall contain the services which represents the HW-blocks.
  The services are strongly associated with the HW they are executing on, but with the aid of the Service Factory Framework, the Services are exchangeable between different deployments.
    Ex. PaSrvc for RU configured for TDD will have a different flavor of the service which will be identified in the service DB.
  Services have no knowledge or dependency on other services
  A service can be shared by multiple controllers, such services are called shared services [e.g. TxLo Service]
Driver Layer:
  The driver layer shall contain the drivers for a specific HW and is accessed by the services via the driver interface (HALI1)
Notes: 2012-10-19
18
Modularization Overview

## Slide 19: Radio SW Architecture - Requirement and Goals
Supports a large number of HW variants
Enable the introduction of new features and functions with relative ease
Enable parallel SW development
  Loosely coupled layers architecture
  Functional encapsulation at each layer
  Clear and well defined interface
  Architectural guidelines

## Slide 20: Radio SW Architecture overview
Radio Application Architecture Description
Notes: Txl SW (TrxCtrl) is included in the Tx Module in this picture, for simplicity reason.

## Slide 21: Mapping to SW realization
…/radiosw/sw/app/om
…/radiosw/sw/app/resource
…/radiosw/sw/app/tx/serviceControl
…/radiosw/sw/app/rx/service
…/radiosw/sw/app/drv/hali1
…/radiosw/sw/app/drv
radiosw/sw/app/commFW/fm
radiosw/sw/app/commFW/eLog
radiosw/sw/app/commFW/activeObject
radiosw/sw/app/ccie_cfhe
radiosw/sw/app/hal/dataBase

## Slide 22: Layer architecture
Common
Libraries
Applications
Functions
eLog, HW log
DB
OSE+XPP
Or
XCS
Hardware
Driver
Radio Driver Interface (a.k.a. HALI1)
Service
Service Control
Resource
R-LRCI/R-ERCI IMPL
Operation Administration Management (OAM)
Board Interface
Radio Device Interface
Common Interface
Antenna Interface
Fault Resource
Handler
Equipment
Resource Handler
Carrier Resource
Handler
File Resource
Handler
Antenna Resource
Handler
Equipment
Module
TX Module
RX Module
Antenna Module
BCI
CBCI
TR
EQMHI
TR
CDCI
DPCL
CDCI
TPA
CDCI
TR
DCI
RMCI
RTFI
AI
CDCI
ANTPI
HAL
RICR
RICI
LTUI
RICRAI

## Slide 23: Radio HW Architecture
Data1
Data2
DAC
Up Conv
TX LO
f0
ADC
DAC
DAC
PA
PA
Peak
Main
Circulator
Band Filter
TOR
DAC
DAC
DAC
Filter Branch
Filter Branch
Filter Branch
Filter Branch
f1
f2
f3
f4
G
G
G
G
G
G
G
G
G
DPD
CPRI I/F
Clipping
DGB
CPU
LNA
LNA
LNA
LNA
LNA
LNA
LNA
LNA
RXA Out
RXA I/O
From RXB
TX/ RXA
RXB I/O
Digital RX
ADC
ADC
RX RF Mix Mod
RX IF Mix Mod
DC/DC
MMI
RXA
Bias-T
ANTP
VSWR
AIB
Digital Front End
TX/ RXB
TX
Analog RX
RIB
RX ADC Mod
FF
LTU
Filter Unit
TOR

## Slide 24: radio sw functions
Initialize the RU during radio board start-up
Configure RU to support the carriers required by the DU - Digital Unit (BaseBand - BB)
Adjust the configuration as result of environmental or carrier power and/or frequency related changes
Supervise RU operation to ensure the health of components and take any needed corrective actions.
Handles measurements functions, e.g. the transmitted and received radio signal power
Supervise the antenna interface, control the antenna devices.

## Slide 25: Device concept
Device id:
Node global identification of a Device Individual in the management interface. It is formed by:
Device Type-Device Individual
e.g ABC-2 (where ABC is the Device Type and 2 is the Device Individual)
Device Set:
All device individuals of the same device type on one device board.
Two different kinds of devices:
Static device:
A Device Individual that which have a fixed address and a fixed capacity. Static devices are created at configuration time.
Dynamic device:
A Device Individual that which does not have a fixed address nor a fixed capacity. Dynamic devices are created during runtime
Device Board
(or AU)
Group
Set
Set
Device
Device
Device Board
(or AU)
Group
Set
Set
Node
Subrack

## Slide 26: Client and server
O&M is implemented between client and server.
A server provides an interface that the client can use.

## Slide 27: Message between client and server

## Slide 28: Multi-client

## Slide 29: OAM

## Slide 30: O&M Layer
O&M
Board Interface
Radio Device Interface
Common Interface
Antenna Interface
BCI
CBCI
TR CDCI
DPCL CDCI
TPA CDCI
TR DCI
RMCI
RFTI
AI CDCI
ANTPI
CCIE
O&M interfaces consist of the following groups:
  WCDMA Board and Device interfaces
    CBCI (Board Control), CDCI (Device Control) and ANTPI (Antenna Port).
  LTE/GSM/CDMA Board and Device interfaces
    BCI (Board Control), DCI (Device Control) and ANTPI (Antenna Port).
  File transfer interfaces

## Slide 31: OAM IF Overview
Notes: 1. ROT-IDCI: Inter-Device Control Interface (IDCI ROT) for Raise Over Thermal, used for measurements of the received signal power
2. The DUS G2 (Generation 2) intends to use the LTE-interfaces as a baseline for the WCDMA O&M. This means that the LTE-interfaces will be used for all RAT’s supported by the Radio Unit. There will still be a need to support the legacy WCDMA interface, though.
3. external alarm, measurement (RMCI), and file transfer (RFTI).

## Slide 32: O&M LAYER IMPLEMENTATION
Static Processes:
  cfhe
  bcProc
  cbcRuProc
  bcLoadHandler
  cbcLoadHandler
  swStoreHandler
  maintStateHandler
  ledProc
  faultManagerProc
Dynamic Processes:
  antpServerProc_
  rotProc
  trProc
  trDcProc
  tpaProc
  dpclProc
  aiProc
  almProc

## Slide 33: SUBSYSTEM INTERFACE
GSW:...radiosw/external/cache (master)> ls
AI_CDCI_CXA104496_1 RDDCI_CXA1107002_1
ANTPIIFU_CXA104491_1 RDSDCI_CXA1106748_1
DCTRIFU_CXA104492_1 RFTI_CXA1106781_1
DPCL_CDCI_CXA104495_1 RMCI_CXA1106780_1
FU_CBCI_CXA104498_1 ROT_IDCI_CXA104500_1
RRU_CBCI_CXA104502_1 RUW_CBCI_CXA104501_1
RU_CBCI_CXA104499_1 LTUIFU_CXA104493_1 TPA_CDCI_CXA104497_1 RDCI_CXA1106778_1 TR_CDCI_CXA104494_1

## Slide 34
An interface is an abstraction of the services provided by a server to one or more clients.
Two interface groups. One used by WCDMA and one used by LTE and GSM.
  CDCI and CBCI for WCDMA
  DCI and BCI for LTE / GSM
Logical devices

## Slide 35: State machine

## Slide 36: SINGAL HANDLING
Group signals are handled by CCIE according to Prod_sigset_struct.cc
DEV_SIG will be routed to device to handle

## Slide 37: Wcdma interface
CDCI-TR
  Manage digital part of carrier related information, measurements and supervision.
CDCI-AI
  Antenna interface. Configure and supervise antenna parts.
CDCI-TPA
  Power amplifier handling. This interface is mostly legacy and has minimal functionality left.
CDCI-DPCL
  Interface for dealing with clipping parameters. Mostly unused on newer radio units. Legacy interface.
CDCI-ALM
  Alarm handling
CBCI-RU
  Radio unit board interface for ”classic” and RUWA units.
CBCI-RUW
  Radio unit board interface for RUW and RUS units.
CBCI-RRU
  Radio unit board interface for RRUW and RRUS units.

## Slide 38: Common signals
Common Signals for group
  XXX_GET_GROUP_CAPABILITY_REQ/CFM/REJ
Common Signals for devices
  Generic O&M Functions
  XXX_CONN_ESTABLISH_REQ/CFM/REJ
  XXX_GET_DEVSET_CAPABILITY_REQ/CFM/REJ
  XXX_AUDIT_REQ/CFM/REJ
  XXX_GO_BACK_TO_STARTING_REQ/CFM/
  XXX_WARM_RESET_REQ/CFM/
  XXX_ENABLE_OPERATION_REQ/CFM/REJ
  XXX_DISABLE_OPERATION_REQ/CFM/REJ
  XXX_SUBSCRIBE_FAULTS_REQ/CFM/REJ; XXX_FAULT_IND; XXX_FAULTCEASE_IND
  Device O&M Functions
  XXX_CONFIG_ADDRESS_REQ/CFM/REJ
  XXX_GET_DEVICE_CAPABILITY_REQ/CFM/REJ
  XXX_SETUP_REQ/CFM/REJ
  XXX_RELEASE_REQ/CFM/REJ

## Slide 39: example
Radio start up and carrier set up
Refer to FD O&M WCDMA CDCI, 3/155 16-CRH 109 0446 Uen

## Slide 40: CCIE
CCIE : Common Communication Interface Engine
The entry point for all signals received in the Radio Unit.
Handles connections between both Node Control (LTE) and Main Processor (WCDMA) to the radio.
Implement a “state machine” who keeps track on clients interface state.

## Slide 41: ccie
RU SW
RU HW
Client (DU/MP)
BCI
DCI
ANTPI
CBCI
CDCI*
IDC
LTE/GSM
WCDMA
CCIE
These common parts for the interfaces are handled by the CCIE (Common Communication Interface Engine).
CCIE is a class library which each interface need to instantiate to be able to communicate with the outside world.
Each interface also need to register all signals, that should be accepted by the interface, with CCIE.
If the client sends a signal which is not registered. This signal will be ignored by the radio.
*) The CDCI interface is divided into 5 sub interfaces which, if used, each has its own CCIE instance

## Slide 42: Ccie class

## Slide 43: Ccie session – multi client
DUL
DUG
DUW
RU
ccieBcInterface
ccieBcSession
ccieBcSession
ccieCbcSession
ccieCbcInterface

## Slide 44: BCI
The main functions of the Board Control Interface (BCI) are:
  Load module handling
  Board state handling
  Board temperature reporting
  Control and reporting of MMI LEDs and button
  HW log read/write/erase
  Board-level fault reporting
  Triggering of board restarts

## Slide 45: BCI: Board Control IF
Notes: 1. bcBase is a emporty class, not impl, instead bcRu is acting as base or main server class. trBcRu used for support new IF TR-BCI used by AAS product.
2. Cbci has two variants, including RUW-CBCI and RRU-CBCI. Both of them inherited from class ’CbcBase’

## Slide 46: DCI
The main functions of the Transceiver Device Control Interface (TR DCI) are:
  Radio capability reporting (output power, frequency range, internal bandwidth, number of carriers, etc…)
  Carrier setup and modification including power, frequency, bandwidth, time alignment and I/Q streams settings
  Handling of antenna port characteristics
  Cross-connect port setup and supervision
  Device-level fault reporting
  Configuration of RF-ports

## Slide 47: DCI: Device Control IF

## Slide 48: Dci device states
DCI State

## Slide 49: Antenna IF
The main functions of the Antenna Port Interface (ANTPI) are:
  Antenna port capability reporting (voltage, supervision, modem, supported antenna line devices)
  Control of voltage and modem
  Connection with antenna line devices TMA or RET
  Sending data to antenna devices
  Antenna system supervision and fault reporting

## Slide 50: Resource Layer
The intention with the Resource layer is to create an inter-module information highway (the modules are not allowed to communicate directly), where the components can pass information between each other and that is needed for the modules.
The Resource layer contains components with hardware independent logic and these components are intended to have a synchronization and orchestration role in the Radio Application. The items to be orchestrated are the different modules, with respect to global events coming from the O&M layer (DU signaling) or to distribute events originating from the modules

## Slide 51: Resource Layer
Fault Manager
Equipment Resource Handler
Carrier Resource Handler
Antenna Resource Handler
Equipment Module
TX Module
RX Module
Antenna Module
Contains the hardware independent logic
Takes synchronization and orchestration role in the Radio SW
Notes: The dashed line are implemented as e.g. Tx/Rx broker.

## Slide 52: Event Subscriber Framework
The Resource layer components communicate using event subscriber framework
The users subscribe to certain events and when these events occur, the subscribers are notified.
The Carrier Resource Handler is (currently) the owner of the framework
Other components will subscribe for the events.

## Slide 53: Controller, Service, Driver
Implements the Module SW interface and provides the logic and orchestrates the events associated with certain functionality.
Responsible for initializing the appropriate services
No dependencies on Platform or HW variants
Can be used as a common component by several controllers.
Exports functionality realized in HW.
Exchangeable between different deployments.

## Slide 54: Service Framework
Service framework provides infrastructure that provide a module with the following:
  Service Factory: Provides the service creation framework -data-driven based-
  Service Container: Provides the framework for service registration and lookup

## Slide 55: Service Database
Module services creation are Database driven. Service definitions are located in the serviceSet DB.
/xxx/mmServices key defines the list of the mmModule services for a specific platform
  mm refers to the module type e.g. tx, rx, etc…

## Slide 56: Service Control Layer Service Layer
The Service Control Layer contains the Service Controllers which are responsible to implement the module interface –to provide upper layers access to the module- and orchestrate logic that can be associated with certain functionality.
The Service layer contains the services which represents the HW-blocks and are strongly associated with the HW they are executing on. An exception to this is the coordination service, which has no direct association with the hardware.

## Slide 57: Shared services
Shared services operate via broadcasting of events to the subscribing controllers -the Controllers subscribe to shared service events at initialization time-.
There are two types of shared services. One to serve a HW block shared between two or more modules of the same type [group of Modules]. And the second type is coordination services to coordinate between multiple modules cycles and prevent deadlocks.

## Slide 58: Module (old hali1 IF)
../sw/app/drv/blockInterface
../sw/app/drv/hali1/blockInterface
../sw/app/drv/hali1
../sw/app/tx/service
../sw/app/tx/serviceControl

## Slide 59: Module (New Hali1 IF)
../sw/app/drv/blockInterface
../sw/app/drv/hali1/blockInterface
../sw/app/drv/hali1
../sw/app/tx/service
../sw/app/tx/serviceControl

## Slide 60: New struct
The driver layer handles device access and publishes logical resources.
The services can concentrate on configuring and using the resources rather than the devices.
HW interface
Driver layer “HW Access”
Driver interface (Resources)
Service layer “The functions”
Driver 2
Driver 3
Service 2
Device 2
Device 3
Driver 1
Service 1
Device 1
HW

## Slide 61: New struct
The driver layer is executing in the context of the calling process and the interface is synchronous method calls.
Driver interface access normally completes quickly.
What to do, with which resource and when to do it, is all up to the services.
Supervision, compensation, fault handling and power save are all functions in the service layers. The driver layer provides the means through which you can realize these functions.

## Slide 62: Driver layer
The purpose of the driver layer is to identify the HW, start the correct device drivers and provide access to the HW through a well specified interface.
We have a collection of device drivers for physical components.
A device driver is generally platform independent and heavily parameterized (Database) to be reusable on any board.
The driver interface hides the device type and device topology from the user.

## Slide 63: Driver Layer
What is not handled by the driver layer?
No protection to avoid dangerous settings (e.g. gain or voltages).
No mechanisms to make sure that we use resources in the correct order to achieve a function (e.g. Rx Gain, Clipping)
No sequences of timed operations on resources.
No arbitration between users that do not agree.

## Slide 64: Driver Layer Cont.
Upper Tier:
  Interface objects mapped to the device drivers
  Common names
  RAW values are converted to human readable values
Lower Tier:
  Device drivers arranged in a dependency hierarchy
  Memory mapped ASICs and FPGAs at the bottom.
  Slave devices above bus masters.
Service Ctrl
Service
Lower Tier
Warp
FPGA
SPI
DAC
GPIO
ADC
Upper Tier
GPIO
Synth
Sensor objects
Blocks
Control objects
Switches
Driver
HW

## Slide 65: Useful Links
RP Radio SW Ericoll
RSW XFT Visualization
Radio Functional Descriptions (FDs) 155 16-CRH 109 0446
Radio Design Documents (DDs) 159 61-CNH 160 6510
Radio Application AD
Doxygen
PD Radio SW WIKI
Acronyms

## Slide 66: Database view

## Slide 67: The purposes of databases
Main objective
  The general purpose of these parameters is to provide possibilities to calibrate, initialize, configure, control, compensate, supervise, measure and report the radio units.
  How to interact with radio’s hardware
    eg whether to use I2C, SPI, or memory mapped I/O
  Hardware configuration settings for particular states
    eg temperature correction tables
  Decision points for triggering certain actions
    eg when to report a voltage fault
  What functionality the hardware supports
    eg what RATs are supported
  The other purpose of the database parameters is to handle different variants of radio HW using the same software regarding internal handling and handling in the interfaces towards the clients..
Advantages
  Simplifies software code
  Avoids hard coding values in software
  Easier to update databases files than to modify code
  Enables hardware and systems teams to make changes without having to modify code

## Slide 68: the database
The Database (DB) is a collection of parameters which contain the information needed to start and run the SW for a specific Radio HW.
There are SW and HW (Production, PA) databases.
  HW DB for calibration data and unit specific parameters
  SW DB for design parameters
All databases are merged into one runtime database.
SW DB
Runtime DB
Prod DB
PA DB
/board/trxDrivers/set char "420"
/board/paDrivers/set char "206"
/420/trxDrivers char "ruwaCsc xppGenIO dcOkSv 2_5V_OkSv ", "warp blockIf warpGenIO spiMaster ", "spiHub ltu10 i2cMaster i2cHub fpgaS90"
/5xx/trxFpgaAiSpiMaster/type char "TrxFpgaSpiMaster" /5xx/trxFpgaAiSpiMaster/deviceTag char "fpga" /5xx/trxFpgaAiSpiMaster/intProcTag char "trxFpgaIntProc" /5xx/trxFpgaAiSpiMaster/regOffset U32 0x300 /5xx/trxFpgaAiSpiMaster/maxNumSlaves U32 2
Hardware DB

## Slide 69: Database example
/5xx/trxFpgaAiSpiMaster/type char "TrxFpgaSpiMaster" /5xx/trxFpgaAiSpiMaster/deviceTag char "fpga" /5xx/trxFpgaAiSpiMaster/intProcTag char "trxFpgaIntProc" /5xx/trxFpgaAiSpiMaster/regOffset U32 0x300 /5xx/trxFpgaAiSpiMaster/maxNumSlaves U32 2 /5xx/trxFpgaAiSpiMaster/bitInIrqReg U8 30 /5xx/trxFpgaIntProc/type char "DeviceIntProcManager" /5xx/trxFpgaIntProc/deviceTag char "fpga" /5xx/trxFpgaIntProc/irq U8 18 /5xx/trxFpgaIntProc/trapReg U32 0x8001 /5xx/trxFpgaIntProc/maskReg U32 0x8000
Key
Parameter
Value

## Slide 70: DB overview
Notes: The external database – often simply called SW external database – with the term “external” is seen from SW point of view and refers to the fact that the database files are provided in txt-files outside of the actual radio SW.
The production database should only have parameters that is changing on a per unit level. The production database is divided into two parts
  Configuration part
  Calibration part.
The content of the production database is written into flash memory of radio hardware during production phase, The configuration part is handling information about power class frequency ranges and so on. The calibration part handles production calibrated values such as gain and frequency correction tables.
*** The production database entries override software database entries with same base name. They cannot be changed after radio units are delivered to customers without a new revision of product.***
The production database and PA production database are also called hardware database (or HW database) since their parameters are written into the radio hardware.
The PA production database shall be loaded to EEPROM. It shall contain powClass, Idq (DPA and Mpa bias), Address, channel and sub channel to all PA components that is digitally controlled - basically all other things that is not placed in the PaSwDb.txt which is part of external database.
The Board parameter file is essentially one file per xRU platform containing parameters controlling the XP platform by describing the HW environment via parameter values.
The component configuration ID database is part of the external database (the external database consists of SW external database and the component configuration ID database.) and consists of 14 files managed by radio HW design team.

## Slide 71: Owner
SW Int Databases
Part of software in PIS and App load files
Content managed by SW team and be modified after radio delivered by build a new .xlf load
SW Ext Databases
Content managed by hardware and system teams
Production Database and PA Database
Content managed by hardware and production teams
Board Parameters
Not strictly a database but serves similar purpose so mentioned here
Content managed by hardware and production teams
Component ID databases
Updated frequently by each new product
Content managed by hardware and SW (board and system) teams

## Slide 72: DB FILES
Database | Database files | Comment
External database Also called SW external database | Clipping.txt dlFilterCoef.txt dlPcFilterCoef.txt gpp3.txt hotSpot.txt paSwDb.txt rxCalib.txt rxFrontEnd.txt sysDataParam.txt tddSwitches.txt temperatureSupervision.txt timing.txt trxPhases.txt txSwDb.txt ulFilterCoef.txt ... ... | Description see chapter 3, can be found in GIT
Database | Database files | Comment
SW internal database Also called SW design database | board.txt channels.txt deviceDrivers.txt driverSets.txt functional.txt protoDbKeys.txt serviceSet.txt supervision.txt | Description see chapter 3, can be found in GIT
Database | Database files | Comment
Production database | Example: Database Update Description RRUS72 B40T, 152 12-KRC161411/1 Board section IQ Start Values DPD Nominal Power & Clip Set Downlink Delay TOR TrxCtrl Rx Calibration Board Parameter updates | Specified in 152 12-KRC spec for each RU product, template file can be found in GIT

## Slide 73: DB FILES
PA Production database | pa_typex_production_Db.txt | Can be found in GIT (not in repo). The wildcard “x” can be one or more characters.
Board parameter file | x_board_para.txt | Can be found in GIT (not in repo). The wildcard “x” can be one or more characters.
Component configuration ID database | aibAdc.txt dpdDevice.txt filterType.txt lna.txt lnaModule.txt ltuModule.txt ram.txt rxAdcModule.txt rxCtrl.txt rxIfModule.txt synth.txt torModule.txt txDac.txt txModule.txt | Specified in 15212- spec for each RU product, template file can be found in GIT (not in repo)
External DB access guidance specified in EAB-14:043436

## Slide 74: Db content
Software searches for base name and uses the key to select which particular parameter to use
For Board Parameters, there are no keys. Radio has one and only one database parameter for each base name
More information on keys is available in the RU DB Design Rules document
The same base name may exist in the Software design database and the Production database but could have different values.
RULE NR.1 : Production DB always overwrite SW DB value if same base name used.
They cannot be changed after radio units are delivered to customers without a new revision of product.
/set4/lte2/pcThreshold U16 67
/set4/lte14/pcThreshold U16 67
clipping.txt
Base name
Key Segment
Value
Parameter
Type

## Slide 75: Database content
Software uses the key to select which parameter to use
The value from the HW database overrides the value from the SW database if the keys are equal
For Board Parameters, there are no keys. Radio has one and only one database parameter for each base name
/set4/lte2/pcThreshold U16 67
/set4/lte14/pcThreshold U16 67
/set4/lte30/pcThreshold U16 67
/set4/lte50_25/pcThreshold U16 64
/set4/lte100_25/pcThreshold U16 64
/set4/lte50/pcThreshold U16 64
/set4/lte100_50/pcThreshold U16 64
Database File
Clipping.txt
Base name
Key
Value
Parameter
Type
Segment

## Slide 76: Driver set
Only a number in production data base (A key to find correct info)
  What drivers that shall be loaded corresponds to driver set is within SW
  Two driver sets exists one for PA and one for TRX
  e.g. /board/paDrivers/set "600"
  /board/trxDrivers/set "601“
What parts of the SW database that shall be loaded also corresponds to a key in the production database
  Example /431/ id_ruType_x.x.x
  It as a function in SW that looks up all database values that have to be loaded on the particular HW. Based on driver set and band info.
In SW the Key can fit into following
  /4XX/id_ruType_x.x.x This can be read as loading parameters for all driver sets that starts with 4 and is of one ru type
  /43X/ id_ruType_x.x.x This can be read as loading parameters for all driver sets that starts with 43 and is of one ru type (If this exists it is chosen higher prio than above)
  /431/ id_ruType_x.x.x The specific driver set 431 shall be used together ruType parameters (If this exists it is chosen higher prio than above)
  Eg. In case that some database parameters need to be modified for bug fix or testing or trouble shooting, the wildcard x may take a specific value 0 or 1 or onwards; while the other database parameters are not concerned and still used the wildcard x.
RULE NR.2 : Software chooses more specific applicable entry over more generic entries.

## Slide 77: Driver Set
Driver Set – a unique numerical identifier for a specific type of HW from a SW point of view.
The same Driver Set can be used for many KRCs.
A 3 digit number:
Driver List – the drivers to start given a specific Driver Set
/422/trxDrivers char "... xppSpiMaster warpSpiHub lnaAdc ..."
4 2 2
Platform
Product Platform
Variant

## Slide 78: parameter priority
Type of RU specified in production database
Software chooses more specific applicable entry over more generic entries
/parameterX U16 0
/4xx/parameterX U16 2
/5xx/parameterX U16 4
/501/parameterX U16 6
/501/BandV/parameterX U16 8
Default value of 0 will be used if none of the other entries are applicable
Value of 2 will be used for all platform IV radios
Value of 4 will be used for all platform V radios that are not using TRX driver set 501
Value of 6 will be used for all platform V radios using TRX driver set 501 that are not Band V
Value of 8 will be used for all platform V radios using TRX driver set 501 that are Band V

## Slide 79: New DB struct
  Driver set tag has limitation and cannot fully be used to identify the product capabilities
      Same trx board in both RUS and AIR
  Identify product DB param by using ruType tag, new struct introduced in G1.
    For product specific parameters complement driverSet by ruType
    Product specific parameters includes;
      Capabilities (eg. /7xx/id_ruType_1.7.x/capabilityDlBw S32 75000)
      Design parameters
      Supervision limits
      Temperature compensations parameters

## Slide 80: Definition of RU Type
ruType_x.y.z
  x: is defined as the variant of RUS, AIR, RRU/mRRU etc.
  y: is defined as Product Specific as shown in the IPP.
  z: is defined as version of product Specific RU.

## Slide 81: RU Type
RU Types: Example:
0 RU Macro Radio Unit
1 RRU Remote Radio Unit
2 AIR Antenna Integrated Radio
3 RIR Repeater Interface Radio
4 RRUS A2 RX only unit, Remote Radio Unit
5 mRRUS micro Remote Radio Unit SDR
6 mRBS micro RBS
7 RRUS E2 TX only unit
8 IRU Indoor Radio Unit
9 AAS Active Antenna System, analog & digital

## Slide 82: FILE REPO
Include all product specific files into the existing repository to the related common file.
e.g all product specific files for timing function will be placed in the same repository as TimingParam.txt

## Slide 83: DL db
clipping contains
  Peak-clipping thresholds for radio units of different RATs and power classes
  Parameters for the rules specified in downlink performance control
dlFilterCoef contains
  DL filter coefficients for various carrier types. The values are measured for various numbers of filter taps depending valid sample rates. There is no product-specific parameter file
dlPcFilterCoef contains
  Filter coefficients of peak filters of clipping functions in CFR (Crest Factor Reduction) in the downlink. The values are measured for various numbers of filter taps depending valid sample rates. There is no product-specific parameter file
paSwDb contains
  Data about supervision limits of currents, voltages and temperatures for PA control
  The values have to be updated before connecting PA and TRX

## Slide 84: Ul db
rxCalib contains
  Data for the receiver part about AGC-related parameters, spectrum rotation, configuration parameters.
  The values have to be updated after necessary measurements before connecting PA and TRX.
rxFrontEnd contains
  Data for supervision limits of LNAs in different frequency band variants and also TDD mode.
  The values have to be updated after necessary measurements before connecting PA and TRX.
ulFilterCoef contains
  UL filter coefficients for various carrier types. The values are measured for various numbers of filter taps depending valid sample rates. There is no product-specific parameter file

## Slide 85: Comm db
sysDataParam is the most extensively used file containing parameters in
  Capability parameters
  Configuration and compensation parameters
Owned by system, shall be updated by system
timingParam contains
  Parameters used for the whole system to get a correct timing in the radio signaling, such as various delays, sub delays and fine delays in the downlink and uplink chains and for frequency bands.
  The values is updated after necessary measurements before RPV (radio performance verification)
The design of database parameters follows
certain rules including the modification of existing database parameters or adding new database parameters. These rules are specified in the design rule document [RU DB DR].
Notes:   Cap: RF port filter branch
  Data port
  Reporting
  TX/RX bandwidth
  No of TX or RX ports
  Duplex mode
  Sub band / full band support,
  PAR (peak-to-average ratio)
  GSM IPM capability
  TX port minimum output power and dynamic power range
  Cross connect, Co-site ports
  HW performance
  Supported carrier types, additional carrier types, and RAT :/id_ruType_1.5.0/Band0/supportedRat char "W L"
  HW specific aux voltages capabilities
  Available antenna port
  Number of static devices reported over the ANTPI
  Conf:Bandwidth information
  Filter branch usage information
  Frequency offsets for NCO
  Internal data link usage
  DL and UL data interface sample rate and sub sample definitions
  DL carrier power default values for compensation and definition of the scaling of baseband signals per carrier type
  Internal data rate at carrier combiner
  Samples per symbol in LTE phase compensation
  MPL settings (0.1dB) relation to 2914
  MPL maximal allowed (0.1dB) gain for WCDMA
  Required power reduction (0.1dB) at Normal to high temp
  Equalizer parameters
  Sub band related parameters
  Seamless Power Level Change (SPLC) parameters
  Frequency hopping support parameters
  WCDMA band specific aux voltages
  Antenna Voltage supervision limits

## Slide 86: stub
Often seen in temporary db files used in early phase dev when real db is not ready or exist
With Key 431/B20
stub/431/B20 will be chosen before values such as 43x/B20 or 4xx/20
stub/4xx/B20 will never be used if 431/B20 or 43x/B20 exists

## Slide 87: DB Coli
Modify prod db value:
$ db write /board/trxDrivers/set -c 551
$ db write /board/paDrivers/set –c 701
$ db prod copy
$ db prod save /board/paDrivers/set
Adding new DB entry
$ db add
$ db resize
$ db write
Delete DB enter
$ db prod del /tor/txA/10W/freqCorTabNoFilter save

## Slide 88: DB Coli
Useful commands
Listing Board Parameters (whole db txt will be printed here)
  $ par get
Listing Production Database
  $ db list prod
Lisitng PA database
  $ db list pa
Listing all used databases
  $ db list * used
Using wildcarding check which trxDriver set used
$ db list *rivers* used

## Slide 89: Resource Names
“TxTempA”
TemperatureSensor
“Tx”
InstanceToken
Legacy Driver Name
Resource Type
Resource Name
Instance
“A”
“Temp”
Instead of embedding the type and instance in the name, we keep them separated.
The name becomes more generic and can be used for resources of different types.
The code is found in radiosw/app/drv/hali1/if

## Slide 90: Instance Token
InstanceToken represent Rx and Tx branches (enumeration ’A’, ’B’, ’C’ in legacy or numerical ’0’, ’1’, ’2’ for AAS)
Can only be created inside the driver layer
Startup routine gets a vector of instance tokens from driver layer by calling Driver::getInstanceTokens() in ’hali1config.cc’
The service uses the instance token to get the correct driver
Used when creating resource objects
  VoltageSensor vdd(ruError,”Vdd”,instanceToken, reportNotFound);

## Slide 91: driverSets.txt – sample entries
Driver SW will be started in order they appear in this list
“HW Initialization Completed” after all drivers have been started
SoC-specific DB entry
Notes: Radio Databases Overview
91

## Slide 92: deviceDrivers.txt – sample entries
Generic SPI Driver (code reuse)
Xenon
(SPI Slave)
Chip Select
Clock
Data
SPI Master Driver (shared with other SPI slave devices)
Xenon
(SPI Master)
Hub Port1
Hub CS3
Notes: Radio Databases Overview
92

## Slide 93: channels.txt – sample entries
Which ADC device
volt (voltage), could also be temp (temperature) or curr (current)
Which channel in ADC device
Which equation to use to convert from ADC reading to voltage value
Parameters used in converstion equation
SiP & SoC use different values
Notes: Radio Databases Overview
93

## Slide 94: rxCalibRru2212.txt – sample entries
At -35.3 degrees Celsius (as measured at Rx temp sensor), gain for rx3 portion of branch B will be increased by 1.14 dB
SW will interpolate between points
ie it assumes a straight line between each set of values in the table
X
Y
for this X value
SW will use this Y value
Notes: Radio Databases Overview
94

## Slide 95: sysDataParam.txt – sample entries
All Band0 radios on all platforms will
support GSM, WCDMA and LTE
PL5.2 BandII supports WCDMA, LTE and GSM
PL?? BandII supports WCDMA and LTE
All other BandII radios support WCDMA, LTE, GSM and CDMA
All Band1 radios on all platforms will
support WCDMA and LTE
An example of DB entries that depend on the carrier configuration:
Notes: Radio Databases Overview
95

## Slide 96: paSwDb.txt – sample entries
PA will be shutdown if MPA temperature exceeds 110 degrees Celsius, Fault will be raised as well
Power level will start to be backed off if MPA temperature excees 90 degrees Celsius
Fault not cleared until temperature drops below 106 degrees (avoids fault toggling)
Notes: Radio Databases Overview
96

## Slide 97: Startup

## Slide 98: Radio app startup
Higher layers SW trigger lower layer
-before start themselves
Notes: ::initOmLayer

## Slide 99: STARTUP OF O&M

## Slide 100: Phantom process
An empty process (does not contain any executable code).
Used to make the communication between processes not residing in the same target as transparent as possible

## Slide 101: Publish interface

## Slide 102: Code:om/startUp/src/startUpProcess.cc
OS_PROCESS(startUp)
{
OMCSF_registerTraceObj_TRACE_OBJ_BCI();
OMCSF_registerTraceObj_TRACE_OBJ_DCI();
OMCSF_registerTraceObj_TRACE_OBJ_ANTPI();
OMCSF_registerTraceObj_TRACE_OBJ_RMCI();
OMCSF_registerTraceObj_TRACE_OBJ_RFTI();
OMCSF_registerTraceObj_AGC_AMPLITUDE_COMP_CONTROL();
OMCSF_registerTraceObj_UL_SUBBAND();
OMCSF_registerTraceObj_TIME_ALIGNMENT_UL();
OMCSF_registerTraceObj_TIME_ALIGNMENT_DL();
OMCSF_registerTraceObj_UL_INTERFERENCE();
OMCSF_registerTraceObj_CLIPPING_DL();
OMCSF_registerTraceObj_UL_FREQ_HOP();
OMCSF_registerTraceObj_UL_DIGITALFILTER();
OMCSF_registerTraceObj_TDD();
OMCSF_registerTraceObj_ZERO_INSERT();
OMCSF_registerTraceObj_TRACE_OBJ_RDBCI();
OMCSF_registerTraceObj_TRACE_OBJ_RDCBCI();
OMCSF_registerTraceObj_TRACE_OBJ_RDSDCI();
OMCSF_registerTraceObj_SV();
OMCSF_registerTraceObj_DATA_COLLECTION();
OMCSF_registerTraceObj_BIN_LOADER();
OMCSF_registerTraceObj_SPI();
OMCSF_registerTraceObj_COLI();
//Create error handler to take care of TMO exceptions
create_error_handler(get_bid(current_process()),
(OSERRH *)block_tmo_error_handler,
200);
initOmLayer();
// startUpTime allows us to collect the time of events in the Startup of the Radio
// so that we can see if new code has am impact on the startup time
// you can set the time using the startuptime shell cmd
startUpTime.ticksInitComplete = get_ticks(); // Startup
stop(current_process());
}

## Slide 103: Code:om/startUp/src/initom.cc
bool initOmLayer()
{
bool startupNormal = initFuncLayer(); //startup all driver according to readed driverset, then TX, RX…modules one by one.
if (!startupNormal)
{
return startupNormal;
}
startupNormal = initResourceLayer();
if (startupNormal)
{
RfSignalResourcesIf::init();
startUpTime.ticksInitComplete = get_ticks();
//TR HS50093
om_layer_success = true;
}
return startupNormal;
}

## Slide 104: Code: func/source/initfunc.cc
bool initFuncLayer()
{
……
……
if (!::StartUp::init()) // Loads SW & Prod Database. Creates and initializes all device driver objects needed for the actual HW unit.
{
func_layer_fail = true;
return false;
}
// init EQP module
if (eqpStartUpPtr == NULL) // code should only be called once per radio init
{……}
//init TRX share module
if (txRxSharedStartUpPtr == NULL)
{……}
//init TX module
#ifdef AAS_WORKAROUND
txStartUpPtr = new Tx::StartUpAAS();
#else
txStartUpPtr = new Tx::StartUp();
#endif
bool txInitRc = txStartUpPtr->init();
if (!txInitRc)
{TRACE_ERROR("Tx::ServiceStartUp fails");……}
// init RX module
// init antenna module
……

## Slide 105: Code: resource/src/initResource.cc
bool initResourceLayer(void)
{
resource_p = new ObjectFramework::StartUp("resource");
if (!resource_p->init())
{
return false;
}
if (!Resource::CscLegacyIf::creator().init(dynamic_cast<Resource::CscResourceIf *>(
resource_p->getObjectLocator().locateObject(Resource::CscResourceIf::OBJECT_ID))))
{
TRACE_ERROR("Failed to init CscLegacyIf");
return false;
}
#ifndef UNITTEST
OMCSF_registerTraceObj_ACM();
#endif
TRACE(1, "initResourceLayer success");
return true;
}

## Slide 106: Driver Layer Start
The SW database (contained in the LMC) is read
The HW (production) database is read from flash
The TRX driver set is read from the database, and the drivers are started one by one
The TRX driver set contains device drivers, channels, supervisions, and other drivers
Failure of the startup causes the failure of Radio startup (restart in AuBoot mode)

## Slide 107: Drivers: General
Configuration of devices is done in three ways:
  Init sequence
  /5xx/txIqDac:x.x/initSeq U32
  0x0000, 0x009E,
  0x0001, 0x000E,
  Pre/post config sequences
  For dependencies between devices
  /7xx/dpdXenon:0/preConfig1/type char "MemMappedDevConfig"
  /7xx/dpdXenon:0/preConfig1/devTag char “xenon:0"
  /7xx/dpdXenon:0/preConfig1/configSeq
  0x02510580, 0x000000FF, 0x00000011, /* Tx branch A DPD_IDLE */
  0x025105C0, 0x000000FF, 0x00000011, /* Tx branch B DPD_IDLE */
  Device driver code

## Slide 108: Drivers: Radio ASIC & GPIO
WarpXX or XenonXX need to be mapped into memory
Initialization of registers
  Through init and pre/postConfig sequences
  Start clocks and release reset for blocks
  etc
I/O pins exist on the Warps, FPGAs, and RX control circuits
Typically default to inputs on power-on
Configured by the driver layer as outputs (“switches”) or inputs (“indicators”)
Switches should be initialized to a safe state
  MPA, DPA off
  etc

## Slide 109: Drivers: LTUs & CPRI link
Local Timing Units lock to the CPRI clock and provide clocks to RX ADCs, TX DACs, etc, and input to synthesizers
There is no reference clock yet (CPRI not configured) so the LTU should be set in free-run mode
Power on SFPs (opto-converters)
  On some platforms this is handled by RICR
Start RICR, which handles the CPRI link
RICR will tell the LTU to lock when a CPRI clock is available

## Slide 110: Drivers: Synthesizers
Also known as local oscillators (LOs)
Some devices are muted at start up
Others must be programmed to a valid frequency

## Slide 111: Drivers: TX & PA
Special care must be taken for TX devices in order not to damage the PA:
  TX VGA and step attenuator must be programmed to maximum attenuation
  After that the TX DACs can be configured and enabled
After all TRX drivers are started, the PA driver set is read from the database
The PA database is read from EEPROM or flash
PA drivers are created based on content of PA database:
  Device drivers for PA control circuits
  Channel and supervision drivers

## Slide 112: Startup
Service Startup
Service Layer
xxxServiceA
:
VoltageSensor
:
VoltageSensor
VddMeasDriver
:
0
InstanceTokens
Driver Layer
VddMeasDriver
:
1
Repository
Driver Interface Layer
HALI-1
Find driver given type, name and instance token
Request all instance tokens
Create service with instance token for branch A or 0 as parameter
Repeat for the next service with the instance token for branch B or 1
Software
Database
xxxServiceB

## Slide 113: Service Layer Start
Modules are started in initFuncLayer
Modules start services based on content of service sets (DB file: sw/config/db/serviceSets.txt)
Services perform additional HW configuration
  Services have additional knowledge about the Radio unit, such as frequency band

## Slide 114: Tx module startup
One time activity of initializing Tx Module Services
Either passes completely where every service starts and initializes successfully or it fails completely
Uses the Service Factory to create the services
Uses the Service Container to register the created services
Service creation is data-driven
Source code located at: sw/app/tx/startup directory

## Slide 115: Service set
TxModule services creation is Database driven
Services definition is located in the Software DB file sw/config/db/serviceSets.txt
/xxx/txServices key defines the list of TxModule services for a particular platform
For each service the following DB keys are defined
  /tx/<service name>/type. Service class type (i.e. class name)
  /tx/<service name/txBranchId. Service branch list (A – H or 0 – 63).
N service instances are created for each branch service (instance name = SERVICE ID + BRANCH ID)
(eg: crfSrv7A = cfrSrv7 + A)

## Slide 116: Service set (ngr g2)
/721/pa721/txServices char
"mplSrv7_2tx channelFilterSrv7_2tx ncoSrv72_2tx txLoSrv72_2tx torLoSrv72_2tx ",
"cfrSrv72_2tx pa1Srv_2tx pa0Srv7_2tx freqHopSrv72_2tx txStepAttSrv7_2tx ",
"txlSrvExt_2tx paSrv7_2tx txBrFaultAdvisor_2tx paComp_2tx txTimingPhaseCtrl_2tx ",
"txCoordinationSrv_2tx bbDataSrv7_2tx cCbSrv7_2tx tmoSchedulerTx tmoFilterTx ",
"diagSrv7_2tx zeroInsertService7_2tx paBranchDelaySrvPf5_2tx bfnAdvanceSrv7_2tx ",
"freqHopTimeOffsetSrv7_2tx fineDelaySrv72_2tx txBranchCtrl_2tx ",
"txBranchMeasCtrl_2tx txPowerSupCtrl_2tx phaseCompSrvPl5_2tx overTempSrv_2tx ",
"cavFilterProtectSrv_2tx circulatorLoadProtectSrv_2tx txBackoffCtrl_2tx ",
"equalizerSrv7_2tx“
/* NGR G2 */
/tx/mplSrv7_2tx/type char "MplSrv7"
/tx/mplSrv7_2tx/txBranchId char "A B"

## Slide 117: Code: statup FUNC/SRC/INITFUC.CC
bool initFuncLayer()
{ ……
……
//Startup is skipped in case of ‘0’ TX branch or empty service set
if (isZeroTxRadio() == true)
{
INFO("Tx Module is not started on zero tx radio");
}
else if (isTxServiceSetEmpty() == true)
{
INFO("Tx Module is not started - empty txServiceSet for this platform");
}
else
{
if (txStartUpPtr == NULL) // code should only be called once per radio init
{
//init TX share module
#ifdef AAS_WORKAROUND
txStartUpPtr = new Tx::StartUpAAS();
#else
txStartUpPtr = new Tx::StartUp();
#endif
bool txInitRc = txStartUpPtr->init();
if (!txInitRc)
{TRACE_ERROR("Tx::ServiceStartUp fails");……}
……
Notes: In RX, In case of startup failure, Startup object is deleted which in turn resets all created services. TX used to be the same behavior, changed now.

## Slide 118: Service startup steps
Query TxModule service list from DB for running platform
Create services
Register services in the Service Container
For each service call its preInitializeService() API
Called by Startup before the service has been created.
For each service call its postInitializeService() API
Save TxBranchCtrl services in the TxBranchRepositry (used by the TxAdpater)
Register TxModule OSE commands
Save TxServiceContainer in TxModCmd (used to locate services)
Save TxServiceContainer in TxServiceRepository

## Slide 119: Code: statup TX/STARTUP/SRC/TXSTARTUP.CC
bool StartUp::init()
{ ……
……
TRACE(1, "TxStartup initialization start");
registerTraceObjs();
vector<string> servicesList;
string txServices = "/txServices";
if (!DataBase::autoGetIfExists(txServices.c_str(), servicesList))
{
TRACE_ERROR(STR("Missing DB entry=%s", txServices.c_str()));
return false;
}
/* Start-up TX services */
if (!traverseTxServiceSet(servicesList))
{
return false;
}
……
(*it)->preInitializeService()
(*it)->postInitializeService()

## Slide 120: Code: statup TX/STARTUP/SRC/TXSTARTUP.CC
bool StartUp::init()
{ ……
……
// All services created, now the power save controller can put
// services into power save mode.
initTxPowerSaveCtrl();
// Create and populate the Repository with txBranchCtrls
createTxBranchRepository();
// Create and populate the Repository with txTimingPhaseCtrls
createTxTimingPhaseRepository();
// Register Tx Module command with the shell command
TxModCmd::registerTxModCmd();
// Need to have access to the service container from the TxModCmd
// to retrieve service instances
TxModCmd::saveServiceContainerPtr(&m_serviceContainer);
//
TxServiceRepository::getInstance().setServiceContainer(&m_serviceContainer);
if (!TxModuleIf::getInstance()->init())
{
return false;
}
TRACE(1, "TxStartup initialization completed successfully");
return true;

## Slide 121: THEN…
bool StartUp::traverseTxServiceSet(const vector<string>& p_servicesList)
{
const std::string dbPrefix("/tx/");
for (vector<string>::const_iterator it = p_servicesList.begin(); it != p_servicesList.end(); ++it) {
const std::string key = dbPrefix + (*it) + "/txBranchId"; // ‘/tx/mplSrv7_2tx/txBranchId’
if (!DataBase::autoGetIfExists(key, branchIdList))
{
if (!startUpTxService(dbPrefix, (*it)))
{
TRACE_ERROR(STR("%s startup failed", (*it).c_str()));
return false;
}
}
else
{
std::vector<std::string>::const_iterator itBranchId;
for (itBranchId = branchIdList.begin(); itBranchId != branchIdList.end(); ++itBranchId)
{
if (!startUpTxService(dbPrefix, (*it), (*itBranchId)))
{
TRACE_ERROR(STR("%s%s startup failed", (*it).c_str(), (*itBranchId).c_str()));
return false;
}
}
}
}

## Slide 122: Code: create service
ServiceFramework::BaseServiceIf* StartUp::createService(
ServiceCommonData& serviceCommonData,
Driver::InstanceToken instanceToken)
{
std::string key = serviceCommonData.getInstanceDbPrefix() + serviceCommonData.getInstanceDbName() + "/type";
std::string serviceClassType;
if (!DataBase::autoGet(key, serviceClassType))
{……}
// Here we get a pointer to a function that creates an instance of the service
ServiceFramework::constructor_t constructInstance =
ServiceFramework::ServiceFactory::create().getServiceClassType(serviceClassType);
if (constructInstance == NULL)
{……}
// Create, register and update service objects with service information from input parameter
RuError err;
ServiceFramework::BaseServiceIf* service = constructInstance(err, m_serviceContainer, serviceCommonData, instanceToken);
if (service == NULL)
{……}
if (err)
{……}
return service;

## Slide 123: Service factory
Startup uses service factory to create the TxModule services
Part of the serviceFW
Provides data-driven service creation framework
serviceFactory.h defines the following main components
  Service constructor Template. Used to create an instance of a particular service
  template <class T>
  ServiceFramework::BaseServiceIf *constructor(RuError &err, ServiceLocatorIf &serviceLocator,
  const ServiceCommonDataIf &attributes,
  Driver::InstanceToken instance)
  REGISTER_SERVICE_IN_SRV_FACTORY Macro. Used to register a service class in the service factory
  #define REGISTER_SERVICE_IN_SRV_FACTORY(x) bool x::m_registeredInSrvFactory = \
  ServiceFactory::create().registerServiceClass<x>(#x);
in service:REGISTER_SERVICE_IN_SRV_FACTORY(Tx::Service::ChannelFilterSrv7
regitserServiceClass() API is called internally when the macro is called to register a service class
getServiceClassType() API is called by the Startup to get a service constructor pointer for a particular service
Code walkthrough…

## Slide 124: Code: create service
ServiceFramework::BaseServiceIf* StartUp::createService(
ServiceCommonData& serviceCommonData,
Driver::InstanceToken instanceToken)
{
std::string key = serviceCommonData.getInstanceDbPrefix() + serviceCommonData.getInstanceDbName() + "/type";
std::string serviceClassType;
if (!DataBase::autoGet(key, serviceClassType))
{……}
// Here we get a pointer to a function that creates an instance of the service
ServiceFramework::constructor_t constructInstance =
ServiceFramework::ServiceFactory::create().getServiceClassType(serviceClassType);
if (constructInstance == NULL)
{……}
// Create, register and update service objects with service information from input parameter
RuError err;
ServiceFramework::BaseServiceIf* service = constructInstance(err, m_serviceContainer, serviceCommonData, instanceToken);
if (service == NULL)
{……}
if (err)
{……}
return service;
Defined in serviceFactory.h
MplSrv7

## Slide 125: Service container
Part of the serviceFW
Provides service registration and lookup framework
serviceContainer.h defines the following main APIs
  registerService()
  unregisterService()
  locateService() based on SERVICE ID
  locateService() based on SERVICE ID + SERVICE VARIANT (same thing as instanceToken but in another domain)
txServiceContainer extends the serviceContainer to provide specific services lookup APIs
  txLocateService() based on SERVICE ID + Branch ID (eg: crfSrv7A)
TxModule extends the serviceCommonDataIf to provide specific service data APIs
  getServiceVariant()
  setBranchId()
  getBranchId()

## Slide 126: DEPLOYMENT view

## Slide 127: Parts needed for getting SW to work
Application SW
  With applicable functions
  With correct databases with at least default/stub values
    SW have to update parts of the SW database to get it work a lot of HW parameters are still updated by SW.
    HW have to go through their databases and do updates when necessary.
Board parameters
Production DB
AU boot
Functional HW

## Slide 128: DEPLOYMENT considerations
The Radio Application is deployed on target HW with limited resources in terms of RAM and flash
The size of the Radio Application deliverable is controlled by including/excluding the FPGA binaries and filtering the database.
The required RAM size is limited by linking in a subset of modules.
The software resides in several slots in FLASH memory.

## Slide 129: FLASH organization
Flash is a non-volatile memory that can be erased and reprogrammed.
The content of flash is preserved over board restarts and power-off periods.
The size of flash, its usage and organization into slots, differ between HW variants, and Radio platforms.

## Slide 130: FLASH organization example
Slot name | SW Type | Provider
LMC0 – AUBoot | 2 | Radio appl.
LMC1 – PIS | 2 | Radio appl.
LMC2 – Radio Application 1 | 3 | Radio appl.
LMC3 – Radio Application 2 | 3 | Radio appl.
Event Log | 3 | Radio appl.
Production Database/PADB | 2 | Factory
HW Log | 3 | Radio appl.
Board Parameters | 2 | XPP/XCS
Node Identity | 3 | XPP/XCS
ABoot | 2 | Radio appl.(removed on Linux PL)
Iboot/(pboot, uboot, uboot_env) | 2 | XPP/XCS

## Slide 131: RADIO LMC
LMC – Load module container
The LMC contains all loadable SW necessary to configure and control the Radio board, including the operating system, middleware, the Radio Application and binaries to load onto the FPGAs.
All the builds use the same Radio application code, but will link in only the drivers necessary for the target HW, thus reducing the memory footprint of the application.
The rationale for building so many different LMC forms is to economize on RAM and flash.

## Slide 132: AUBoot
Minimized variant of the LMC whose task is to assist the client with loading and starting the required LMC.
Delivered together with the HW as a type 2 SW.
The first SW started on Radio after power-on and cold restart.
No radio resources are activated by the AUBoot.
Only the drivers to load the COM FPGA, setup the LTU and the synthesizers are linked into this variant of the Radio Application.

## Slide 133: AUBoot (2)
A limited subset of O&M procedures:
  Fetching board capabilities
  Acquiring resources (multi-client locking)
  Fetching HW PID
  All procedures concerning the LMC (inventory list, fetching the running LMC identity, loading, selection, deleting, retrieving the compatibility list?)
  MMI/LED handling
  Setting real time clock

## Slide 134: Pre-installed SW (PIS)
Similar to the Radio Application, backwards compatible on a black box level
Distributed together with Radio HW as Type2 SW, factory loaded in flash slot 1, protected
PIS is loaded into RAM and started if there is no other suitable Radio Application LMC available in the base station.
The goal is to enable selling of new radio HW (which requires new SW) to customers running older SW

## Slide 135: Design WoW

## Slide 136: How it all started
we needed to improve HW/SW decoupling and that we should implement a HALI-1 interface. Furthermore, it was also driven by new modelized SW architect. According to the system definition, the HALI-1 interface is an interface towards low level device drivers. It would facilitate replacement of one device with a device of a similar class, e.g. replace an SPI connected ADC with another one.
The general idea was that HALI-1 would make it easier to support new radio variants.

## Slide 137: Old story
Device driver interface already exist. It wasn’t a problem to support new devices. But We want to have an interface on a slightly higher level of abstraction where the objects were not devices but “resources” with a property.
Our experiences with the radio told us that the device oriented interface isn’t enough to hide common HW changes which are bigger than just the replacement of a device.

## Slide 138: Level of Abstraction
The DPD can be in the Xenon or in an FPGA, it’s not the chip we want to publish, it’s the DPD block.
Two 4-channel ADCs can be replaced with one 8-channel ADC. It’s the channels (I/Os) that are common between designs, not the number of devices.
Xenon
DPD
FPGA
Device level
Resource level
DPD
ADC 4 ch
ADC 4 ch
ADC 8 ch
Temp
LNA
Temp
LNA

## Slide 139: The Driver Interface aka HALI-1
Eventually there was a consensus where the higher abstraction level of our driver interface, and the focus on resources rather than devices, was chosen as the way forward.
Given that these resources are common in many radio designs, they will facilitate development of new radio variants.
New driver interface (aka HALI-1) on top of our old developed as part of the RU SW modularization.

## Slide 140: Design advantages
Easy to use for SW designers
  Small, simple interfaces
  Type safety
  Object based
Designed for testability
  Unit test framework with mock objects
  Small testable objects, no inheritance
  Command line access to all resources
Designed for scalability
  Easily scalable to more Rx/Tx branches
  A branch is never explicitly specified in the driver interface
  New interface can be added on for every new RU without legacy impact.

## Slide 141: Interface Objects
Two different categories: Resources and Blocks
Resources represent components, analog and digital I/O.
Blocks are more complex and usually reflect functional modules.
Resource
Block
X
X

## Slide 142: Blocks
A block is a collection of registers, a bit pattern, that can exist as one or many instances and in any ASIC or FPGA.
There is a 1-to-1 mapping between HW blocks and SW blocks (scaling is normally per branch).
A new HW implementation could still require a new block driver implementation even though the block interface remains the same.
The code is found in radiosw/app/drv/hali1/if/blockinterface

## Slide 143: Blocks
The purpose of a block interface is to hide the location of the HW block and details like field widths and bit order.
New functionality in a HW block means that it will be treated as a new block with no relation to previous versions other than possibly the name.

## Slide 144: Blocks Cont.
ON
OFF
STAT
ON
OFF
F_MEAS
F_COMP
STAT
FPGA 1
Warp
FPGA 2
Radio 1
Radio 2
My_Block
Driver Layer &
HW
New revision
My_Block_2
Xenon
Radio 3
on() off() status()
MyBlock
on() off() status()
MyBlock
on() off() status()
MyBlock
on() off() status()
MyBlock
on() off() status() measure() compensate()
MyBlockV2
on() off() status() measure() compensate()
MyBlockV2
Driver Interface Layer
Service:A
Service:B
Service:A
Service:B
Service:A*
Service:B*
0x120
0x124
0x128
0xA1000
0xA1004
0xA1008
0xA100B
0xA1010

## Slide 145: Legacy Blocks
The legacy Block Interfaces are a union of all the functions of all the versions of the block. The block implementations are forced to implement a lot of empty methods that do not apply to the specific HW.
The long-term goal for the blocks is that they will be smaller, more specific and hence more stable for any given HW block.

## Slide 146: Blocks – One Large interface
Service 1
Driver 1
f1()
f2()
f3()
f4()
Service 1
Driver 2
f1()
f2()
f3()
f4()
Service 1
Driver 3
f1()
f2()
f3()
f4()
HW 1
HW 2
HW 3
HW interface
Driver interface
Impact on legacy implementation and interface
The interface for HW 1 and HW 3 have no similarities but the legacy remains...
1
2
3
2
4
4
(Legacy Radio SW approach)

## Slide 147: Blocks – Small Interfaces
Service 1
Driver 1
f1()
f2()
f3()
Service 2
Driver 2
f2()
f4()
Service 3
Driver 3
f4()
HW 1
HW 2
HW 3
HW interface
Driver interface
Small interfaces that are stable once created.
No impact on legacy when adding support for new HW.
1
2
3
2
4
4
The intent is not to hide functional changes from the services!
v1
v2
v3

## Slide 148: Code: Service case1 (resource)
class PowerConsumptionMeas
{
Driver::VoltageSensor* pVolt;
Driver::InstanceToken m_instanceToken;……
……
……
public:
PowerConsumptionMeas (Driver::InstanceToken in) : m_ instanceToken(in), pVolt(NULL) {};
……
……
bool PowerConsumptionMeas::postInitializeService()
{
if (DataBase::autoGet("/DCVoltageSensor", voltageChName) == false)) {TRACE_ERROR (…); return false;}
RuError err;
pVolt = new Driver::VoltageSensor(err, voltageChName.c_str(), m_instanceToken);
if (err)
{
TRACE_ERROR(err.getError().c_str());
or INFO(STR("ABN:%s, %s", __func__, err.getError().c_str()));
}
return true;
}
……
……
bool PowerConsumptionMeas::sample()
{
Voltage v = pVolt->read(VruErr);
}

## Slide 149: Code: Service case2 (resource)
class AntVCCService
{
Driver::VoltageSensor* m_voltageMeas;
Driver::InstanceToken m_instanceToken;
const std::string voltageSensorName("Antenna");
……
……
public:
AntVCCService(Driver::InstanceToken in) : m_ instanceToken(in), m_voltageMeas(NULL) {};
……
……
bool AntVCCService::postInitializeService()
{
RuError err;
m_voltageMeas = new Driver::VoltageSensor(err, voltageSensorName, m_instanceToken);
if (err)
{
TRACE_ERROR(err.getError().c_str());
}
return !err;
}
……
……
bool AntVCCService::measure(RuError &err)
{
m_voltage = m_simulationOn ? m_simulatedVoltage : m_voltageMeas->read(err);
}

## Slide 150: Code: Service case 3 (block)
class Pa0Srv7
{
Driver::BlockInterface::Pa0V2* m_pa0Driver;
……
……
public:
Pa0Srv7 (Driver::InstanceToken in) : m_pa0Driver(BlockInterface::pa0V2(err, in)) {};
……
……
bool Pa0Srv7::setAdjust(uint8_t fbId, uint32_t pa0AdjLevel) {
RuError err;
m_pa0Driver->safeSetAdjust(ruErr, fbId, pa0AdjLevel, m_PowerRampVal);
if (err)
{
TRACE_ERROR(err.getError().c_str());
}
return !err;
}
……
……

## Slide 151: wOw BETWEEN app sw AND board
Include board team!(aka the driver team in global track)
  Whenever there are any changes regard to drv layter IF or impl, please present new design choices to board, site together to design a good SW for the future.
  Always Invite them to code reviews when new IF impls are created.
  Always Invite them to code reviews when new IF are created.
Good documentation (Mainly in doxyen)
Be aware of the SW impact and select the cheapest/best solution when given multiple choices.

## Slide 152: TR report
https://lmr-radiosw-mantis.rnd.ki.sw.ericsson.se/mantis/

## Slide 153: Tx Module

## Slide 154: TX Module Overview
TX Freq Conf
DL Subband
DL Filter
DL Timing
TXAttCtrl
TX Carrier Power
Power Class
PA
DL FreqHop
TRXCtrl
TDD SwitchCtrl
CFR
MPL
DL Data
TxBranch
TXCarrier
Carrier Resource Handler
I/F Objects implemented through R-LRCI
Logical Resource Objects
Services + Drivers
Resource Layer
Service Control Layer
Service + Driver Layer
TX Branch Control
Filter Branch
Filter Branch
Filter Branch
Filter Branch
f1
f2
f3
f4
G
G
G
G
Data1
Data2
G
G
G
G
G
DAC
Up Conv
DPD
CPRI I/F
Clipping
TX LO
f0
ADC
DAC
DAC
DGB
PA
PA
Peak
Main
Circulator
Band Filter
TOR
CSC
DL Eq
DAC
DAC
DAC
TR DCI
O&M Layer
Notes: For simplicity reasons, the Service and Driver layers are combined into one layer compared with previous picture.

## Slide 155: TX

## Slide 156: CLASS DIAGRAM – TX FILTER BRANCH SERVICES
../sw/app/drv/blockInterface
../sw/app/drv/hali1/blockInterface
../sw/app/drv/hali1
../sw/app/tx/service
../sw/app/tx/serviceControl

## Slide 157: CLASS DIAGRAM – TX BRANCH SERVICES
../sw/app/drv/blockInterface
../sw/app/drv/hali1/blockInterface
../sw/app/service/txlSrv/If
../sw/app/tx/service
../sw/app/tx/serviceControl
../sw/app/drv/hali1
../sw/app/service/txlSrv/TxlProxy

## Slide 158: CLASS DIAGRAM – SHARED TX SERVICES
../sw/app/tx/service
../sw/app/tx/serviceControl
../sw/app/drv/hali1
../sw/app/drv/blockInterface
../sw/app/drv/hali1/blockInterface

## Slide 159: TX MODULE SW RESOURCES
A carrier is modeled as a Filter Branch Set in Tx Module
Filter Branch Set is a list of Filter Branches with its associated carrier configuration data.
Filter Branch id range used within Tx Module is 0..7.
Hali-1 driver interfaces use filter branch id range 0..7 as input
Port swapping for PL5 occurs at Driver layer
Legacy filter branch id conversion from 0..15 to 0..7 per Tx Branch is done by Tx Adapter
Carrier id and carrier type id are not used within Tx Module
When a carrier is setup the configuration information is stored in a record and a unique FBS id is assigned to it
Carrier id is stored in the associated FBS record for later use as a reference for sending messages back to Carrier Control eg. Activation Indication
When a carrier is released the associated FBS record is removed.

## Slide 160: TX MODULE HW RESOURCES
HW resources are configured and managed by Services
HW configuration topology is transparent to the Tx Branch Controller
The status and configuration of HW resources are not retained by Services – once the HW change occurs, the Service forgets its configuration
The status and configuration of such HW resources as TxLo, TorLo and Pa is stored in and maintained by the Resource Handler and can be accessed by all Services by means of well defined interfaces

## Slide 161: TX BRANCH CONTROL
SW location: ../app/sw/tx/serviceControl
Active Object
controller for actions on each Tx Branch.
platform and hardware independent
state machine driven
controls all transmit carriers (FBSs). This includes requests for setup, activate, deactivate, release, frequency modify and power modify.
for all carrier operations it triggers all the required steps on TX services.
the dependency between steps or the service dependencies is embedded in the steps that TxBranchCtrl follows.
does not perform validation of carrier configuration coming from Carrier Control

## Slide 162
Downlink frequency
26/102 62-CNH 160 6510
Purpose
  Configures NCO, TX_LO, TOR_LO to achieve wanted RF frequency.
Description
  TX LO frequency: Center frequency of the used DL bandwidth.
  NCO frequencies: Offset frequency for each carrier vs. TX LO.
  TOR LO frequency: Down converting frequency for the DPD loop. Set to fixed offset to TX LO.

## Slide 163
DL Filter
27/102 62-CNH 160 6510
Purpose
  Achieve signal RRC (Root Raised Cosine)shaping thus reduce ISI
Description
  Select/Configure corresponding coefficients for different carrier types: GSM (200kHz), WCDMA (3.8-5MHz) and LTE (1.4, 2.5, 3, 5, 10, 15, 20MHz).

## Slide 164
DL time alignment
38/10262-CNH 160 6510
Purpose
  Adjust/align total delay from node reference point (T_RP) to Antenna Reference Point (ARP) in radio so that the carrier user data reaches the antenna at a given BFN time.
Description
  Total delay is the sum of (1) CLK delay from T_RP to the RRU, (2) CLK delay within COM-FPGA, (3)RRU internal digital/analog delay and (4) external delay from RRU to ARP.
  The compensation is done in the ASIC.

## Slide 165
Crest Factor Reduction
25/102 62-CNH 160 6510
Purpose
  PA capacity shall cover Pnom+PAR@0.1% probility
  Lower PAR  lower cost and higher efficiency
Description
  MPLC: Mean Power Loss Compensation compensates for the small reduction of power introduced by the clipping

## Slide 166
TRX control
49/102 62-CNH 160 6510
Purpose
  Runtime conpensate compression characteristic of PA HW
  Conpensation gain changes caused by temperature/frequency
PA compression curve

## Slide 167
DL Power/Gain Compensation
58/102 62-CNH 160 6510
Description
  DL Pcomp controls output power setting and gain compensation in DL.
  PA0 sets correct nominal output power per carrier/fb for G/W/L
  PA0 also compensates (Front End filter) output power per carrier within IBW (20MHz) for W&L and static GSM.
  PA1 sets correct DPD input power for G/W/L.

## Slide 168
Power Amplifier Control and Supervision
24/102 62-CNH 160 6510
Purpose
  Set to best bias voltages depending of power class
  Control PA on/off for TDD or power saving

## Slide 169: DS
DS 25/102 62-CNH 160 6510 Crest Factor Reduction
DS 20/102 62-CNH 160 6510 DL Data
DS 44/102 62-CNH 160 6510 DL Equalizer
DS 27/102 62-CNH 160 6510 DL Filter
DS 77/102 62-CNH 160 6510 DLPerfCtrl
DS 38/102 62-CNH 160 6510 DL Time Alignment for RU
DS 29/102 62-CNH 160 6510 DL Subband
DS 4/102 62-ROP 101 089/1 DL Mixer, NCO and Carrier Combiner
DS 28/102 62-CNH 160 6510 MPL
DS 49/102 62-CNH 160 6510 TRX Control
DS 88/102 62-CNH 160 6510 TX Analog Gain and Attenuation Control
DS 81/102 62-CNH 160 6510 TX Branch Control
DS 58/102 62-CNH 160 6510 TX Carrier Power
DS 26/102 62-CNH 160 6510 TX Frequency Configuration
DS 85/102 62-CNH 160 6510 TX Main
DS 102 62-CNH 160 6510 TX Module Startup and Initialization
DS 24/102 62-CNH 160 6510 TX PA Control and Supervision
DS 46/102 62-CNH 160 6510 TX Power Class

## Slide 170: Filter Branch Services
The notion of Filter branch services pertains to services which are responsible for configuration of digital filter branches on the digital ASIC (e.g. WARP, iWARP, Xenon) HW blocks.
The Tx Module supports such filter branch services as MplSrv, FreqHopSrv, and Pa0Srv just to mention few.
Filter branch services configure filter branches only and have no notion of Filter Branch Sets (FBS) or carriers.

## Slide 171: Digital asic – filter branch
Each filter branch does the digital signal processing for one carrier (of certain bandwidth):
  GSM, WCDMA, LTE (FDD or TDD), CDMA
Description of Parameter | WARP 1.7 | WARP 3.0 | WARP 3.5 | iWARP 3.5 | Xenon1.0
Total number of filter branches in one ASIC | 4 | 16 | 16 | 16 | 24
Number of ≤ 5MHz Filter Branches | 4 | 8 | 0 | 0 | 0
Number of Narrowband Filter Branches (GSM) | 0 | 8 | 0 | 0 | 0
Number of ≤ 10MHz Filter Branches | 0 | 0 | 16 | 16 | 0
Number of ≤ 20MHz Filter Branches | 0 | 0 | 0 | 0 | 24
Supports Fullband LTE carriers (10, 15, 20 MHz) | no | yes | yes | yes | yes

## Slide 172: TX BRANCH SERVICE
The notion of Branch services pertains to Tx branch services which are responsible for the configuration of analog and digital HW components belonging to a particular RF Tx branch.
Branch services use Filter Branch Sets (FBS) in the algorithmic calculations.
The Tx Module supports such branch services as PaSrv, Pa1Srv, and TxlSrv to mention few.
Branch services configure analog parts such as PA and step attenuator as well as such HW blocks on the digital ASIC as CFR and PA1.

## Slide 173: TX Service topology
The Tx Module supports the following service types:
Filter Branch Services – services which configure the digital ASIC HW blocks with digital filer branches. An example of such service is the Pa0Srv.
RF Branch Services – services which configure HW components specific to a particular TX branch. An example of such service is the cfrSrv.
Shared services – services which are common to multiple TX branches. An example of such service is the TxLoSrv. Shared services typically manage HW components that are common to multiple TX branches.

## Slide 174: Tx shared service
The notion of Shared services pertains to Tx Branch services shared between multiple instances of Tx Module (Tx Branch Controllers).
The Tx Module supports such shared services as TxLoSrv, TorLoSrv, PaSrv and TxCoordinationSrv.
The TxCoordinationSrv coordinates functional cycles between set of branches sharing common HW to ensure no deadlocks.
With the exception of the TxCoordinationSrv, a shared service manages a HW component that is common to multiple TX branches (TxCoordinationSrv is a special service that is not directly mapped to any particular hardware component).

## Slide 175: Tx shared service
Multiple Tx Branch Controllers subscribe to shared service events at radio start-up time.
Shared services use data from each subscribing Tx Branch Controller (Resource Handler).
Controllers pass the reference to their Resource Handler to shared services at service initialization time.
Shared services operate via broadcasting of events to the subscribing controllers
Multiple Tx Branch Controllers subscribe to shared service events at radio start-up time.

## Slide 176: Shared services – TX Example

## Slide 178: Subband Backgroud
Originally created for RU platform 4 to enable 10, 15 and 20MHz LTE (FDD or TDD) carriers by combining multiple 5MHz Subbands.

## Slide 179: Temperature Compensation
Adjust drain voltage PA_Vdd to optimize PA efficiency.
Set a optimal digital word into the DAC that controls the drain voltage.
Started upon PA On, takes place periodically until PA Off.
Each PA_Vdd voltage is temperature compensated separately if more than one TX branch.

## Slide 180: DAC towards Temperature

## Slide 181: Sequence Diagram

## Slide 182: Frequency Compensation
In some frequency bands there is a need to increase the drain voltage on the band edges.
If no freqCompTable in pa_production_db, temperature compensation only.
Started upon PA On together with temperature compensation, takes place periodically until PA Off.

## Slide 183: ACTIVE OBJECT / CURRENT OSE PROCESS PRIORITIES
An Active Object is an object that owns an OSE process and can initiate control activity.
0 is OSE highest priority, 31 is OSE lowest priority
trProc and trDcProc (Carrier Control) – OSE priority 15
  no change to current setting
TxBranchCtrlA/B, PaSrvA/B, TxLoSrv, TorLoSrv – OSE priority 14
  ensures that LPLC/SPLC frequency and power change operations will get to run before majority of processes including Carrier Control
  RICR_sup_link_1/0 and RICR_fault_handler run at this priority
TxCoordinationSrv (Cycle Coordinator) – OSE priority 16
  will delay cycle start until Carrier Control completes processing of all carrier requests (Rx and Tx) buffered in the OSE queue
  maximizes buffering of Tx carrier events
TxlProcBranchA/B – OSE Priority 10

## Slide 184: REFERENCE
TX DD (alive and heavy, but good detail info…)
https://erilink.ericsson.se/eridoc/erl/objectId/09004cff88b5b867?docno=4/15961-CNH1606510Uen&action=current&format=msw12
Doxygen documentation
https://fem007-eiffel003.rnd.ki.sw.ericsson.se:8443/jenkins/view/RadioSW/view/Doxygen/job/radio_doxygen_radiosw/doxygen/
RA Radio/Product Documents wiki page
https://lte-wiki.rnd.ki.sw.ericsson.se/mediawiki/index.php/RA_Radio/Product_Documents

## Slide 185: CARRIER EVENT PROCESSING

## Slide 186: TX ADAPTER
SW location: ../sw/app/adapter/tx
Subscribes to carrier control events on behalf of TxBranch controller (see next slide)
Converts legacy carrier data structure to tx data structure when carrier event is sent to Tx Module
  performs SW database lookups for carrier type based keys (signal BW, power compensation, bb scaling etc)
  Design Rule: carrier type should not be used within Tx Module
  converts legacy filter branch id to filter branch id range 0..7
Provides API for 0-insertion via by CSC
Provides API for sending Activation Indication/Power Modify Indication from Tx Module to Carrier Control

## Slide 187: TXADAPTER - CARRIER EVENT SUBSCRIPTION
TxBranchCtrl subscribes to carrier events via the TxAdapter with the CR_SUBSCRIPTION_PRIORITY_SETUP_CARRIER_DIG priority.
  enum CarrierSubscriberPriority_t
  { CR_SUBSCRIPTION_PRIORITY_HIGHEST = 1,
  CR_SUBSCRIPTION_PRIORITY_CONFIG_DATA_STREAM_DIG = CR_SUBSCRIPTION_PRIORITY_HIGHEST,
  CR_SUBSCRIPTION_PRIORITY_TDD_SWITCH_CTRL = CR_SUBSCRIPTION_PRIORITY_HIGHEST + 1,
  CR_SUBSCRIPTION_PRIORITY_SETUP_CARRIER_DIG = CR_SUBSCRIPTION_PRIORITY_HIGHEST + 2, TxBranchCtrl Subscriber Priority
  CR_SUBSCRIPTION_PRIORITY_SETUP_POWER_COMP = CR_SUBSCRIPTION_PRIORITY_HIGHEST
  CR_SUBSCRIPTION_PRIORITY_TIME_ALIGN_SETTINGS = CR_SUBSCRIPTION_PRIORITY_HIGHEST + 4,
  CR_SUBSCRIPTION_PRIORITY_NCO_SETTINGS = CR_SUBSCRIPTION_PRIORITY_HIGHEST + 5,
  CR_SUBSCRIPTION_PRIORITY_FREQHOP_SETTINGS = CR_SUBSCRIPTION_PRIORITY_HIGHEST + 6,
  CR_SUBSCRIPTION_PRIORITY_FILTER_SETTINGS = CR_SUBSCRIPTION_PRIORITY_HIGHEST + 7,
  CR_SUBSCRIPTION_PRIORITY_PHASE_ALIGN_SETTINGS = CR_SUBSCRIPTION_PRIORITY_HIGHEST + 8,
  CR_SUBSCRIPTION_PRIORITY_LOWEST = CR_SUBSCRIPTION_PRIORITY_HIGHEST + 9
  };
TxBranchCtrl subscribes to the following carrier events via the TxAdapter:
  CR_SUBSCRIPTION_EVENT_CARRIER_RELEASED
  CR_SUBSCRIPTION_EVENT_CARRIER_SETUP
  CR_SUBSCRIPTION_EVENT_CARRIER_ENABLED
  CR_SUBSCRIPTION_EVENT_CARRIER_DISABLED
  CR_SUBSCRIPTION_EVENT_CARRIER_MODIFY
  CR_SUBSCRIPTION_EVENT_CARRIER_POWER_MODIFY

## Slide 188: EVENT PROCESSING - CYCLE FLOW
Cycle is a sequence of operations required for one TxLo change and one power change on one or two tx Branches
Two cycles:
  Power Change Cycle
  Frequency Change Cycle

## Slide 189: EVENT PROCESSING
Services process data derived from multiple carrier events which arrived prior to the cycle start
Carrier events may arrive during a cycle while services are in the process of frequency change or power change
In order to avoid collisions of the new arriving carrier event data with the carrier event data services are currently processing, two sets of carrier data exist:
  set of data committed to the currently running cycle: this data is locked in - it is not updated throughout the cycle
  set of buffered data: this data is updated as new carrier events are arriving during the cycle
At the beginning of each cycle, the buffered data is moved to the committed data.

## Slide 190: EVENT PROCESSING - DATA FLOW DURING CYCLE

## Slide 191: DATA FLOW DURING CYCLE
At the beginning of each Freq change cycle Buffered data is transferred to Committed data.
At the end of each Power change cycle, Buffered data is evaluated for new cycle trigger.
If new cycle required:
  send trigger to Tx Coordination service.
  while waiting for Tx Coordination service for response, Tx BranchCtrl keeps updating the Buffered data when new events are coming.
  once the Tx Coordination service trigger to start Freq change cycle arrives, commit the Buffered data i.e. compare and evaluate the current Buffered data and the Committed data used in the previous cycle.
  Both Buffered and Committed Data sets are the same at the beginning of each Freq change cycle.
  proceed with the cycle
If no new cycle required:
  update the Buffered data as new events are incoming
  re-evaluate for new cycle
If cycle trigger comes due to another branch request:
  commit the Buffered data

## Slide 192: EVENT PROCESSING – RESOURCE HANDLER
Resource Handler is the owner of the Buffered and Committed data and operations on it.
Resource Handler is responsible for:
  allocation/deallocation of resources
  resource state and configuration updates
Tx Branch Control triggers operations on RH to update the Buffered data based on event received from Carrier Control.
Tx Branch Control is responsible for the Commit operation i.e. based on Buffered and Committed data from the last cycle. Tx Branch Control figures out new Committed data contents. Resource Handler updates the Committed data.
Tx Branch Control owns the algorithm for committing data. RH owns the contents of the data.

## Slide 193: TXCOORDINATIONSRV
Active Object
SW Location: ../sw/app/tx/services/txCoordinationSrv
Coordinates frequency and power change cycle(s) for all Tx Branch controllers
State machine controlled
Ensures the correct ordering of frequency and power changes by an API that the TxBranchCtrl registers with.
The service control layer requests the cycle when a carrier request requires one. When the state of Tx Coordination is ready it will begin the cycle.
If there is a cycle underway it will be blocked pending the completion of the current cycle.
To start a cycle Tx Coordination sends notifications through the API to do frequency changes.
This is the trigger for the service control layer to do the actual frequency change steps by controlling the required services. E.g. txLo, torLo or ncoSrv.
Tx Coordination is not aware of which services are used or their order. Once the service controller completed the frequency change it will notify Tx Coordination that it is done.
Only at this point will Tx Coordination trigger the power change by using its API to signal to the service control layer to start a power change cycle. This proceeds in the same way as a frequency change.
The control layer works with the services to do any power changes and then signals Tx Coordination that it is finished the power change cycle.

## Slide 194: What is changed and unchanged (FOR FSM imported into Tx module)
We moved code from a big class to some small classes.
  The change cycle FSM is added
  Two helper classes are added for the FSM.
  Add two helper class for POWER_CHANGE state. One for LPLC and the other for SPLC.
No any function change is expected in the resturcturing.
The restructuring does not change any external behavior of TxBranchCtrl.
  For all sequence diagrams in “TX Module DD”, TxBranchCtrl is still original TxBranchCtrl, the resturcturing has no DD impact.

## Slide 195: Tx Branch Ctrl and its helpers
Notes: Notes:
TxChangeCycleFsm is the FSM class, which provides two interface: TxChangeCycleFsmIf and TxChangeCycleFsmInternalIf.
  TxChangeCycleFsmIf is to be used by TxBranchCtrl.
  TxChangeCycleFsmInternalIf is to be used by all change cycle states.
All change cycle states have a base class TxChangeCycleState.
A TxChangeCycleFsm instance owns below instances:
  The instances of all change cycle states. They’re used by a pointer of their base class, i.e. TxChangeCycleState.
  An instance of TxChangeCycleBasicHelper.
  An instance of TxChangeCycleHelper.
A TxChangeCycleFsm instance passes “this” pointer of type TxChangeCycleFsmInternalIf to instances of all change cycle states.
A TxChangeCycleFsm instance may pass instance pointers of either TxChangeCycleBasicHelper or TxChangeCycleHelper to the instance of any change cycle state if necessary.
A TxChangeCycleFsm instance passes instance pointers of TxChangeCycleBasicHelper to instance of TxChangeCycleHelper.

## Slide 196: Change cycle states
Change cycle states:
enum TxBranchCtrlTxChangeCycleStateEnumType
{
TX_BRANCH_CTRL_TX_CHANGE_CYCLE_STATE_IDLE,
TX_BRANCH_CTRL_TX_CHANGE_CYCLE_STATE_INIT,
TX_BRANCH_CTRL_TX_CHANGE_CYCLE_STATE_PREPARATION,
TX_BRANCH_CTRL_TX_CHANGE_CYCLE_STATE_TX_LO_CHANGE,
TX_BRANCH_CTRL_TX_CHANGE_CYCLE_STATE_POWER_CHANGE,
TX_BRANCH_CTRL_TX_CHANGE_CYCLE_STATE_FILTER_BRANCH_FINALIZATION,
TX_BRANCH_CTRL_TX_CHANGE_CYCLE_STATE_TXL_FINALIZATION,
TX_BRANCH_CTRL_TX_CHANGE_CYCLE_STATE_TXL_RESTART_FINALIZATION,
TX_BRANCH_CTRL_TX_CHANGE_CYCLE_STATE_FINALIZATION // add it as per input
};
We found state transitions by searching “setTxChangeCycleState” in base code.
We named events based on function names where the state transitions happen.

## Slide 197: The FSM

## Slide 198: Behavior change
There is a subtle behavior change:
  Before the restructuring, we set To-state of change cycle no matter what is the From-state, e.g.
  setTxChangeCycleState(TX_BRANCH_CTRL_TX_CHANGE_CYCLE_STATE_PREPARATION);
  After the restructuring, the From-state and To-state of all state transitions are explicitly defined.
We have checked that all reasonable state transitions are implemented.
  But if an event is received in an unexpected state, the behavior is different between old and new implementation.

## Slide 199: Set state
Search “m_fsm->setState” to find all state transitions now.
onExit is called when we exit a state.
onEnter is called when we enter a state.
“rollback” is added to keep legacy behavior.
  In TxBranchCtrl::changeFinalize of old code, change cycle state is not changed if the function needs to return false. So previous state is kept.
  The code of TxBranchCtrl::changeFinalize is moved to TxChangeCycleStateFinalize::onEnter of new code. We need to rollback to previous state when TxBranchCtrl::changeFinalize return false.
  Some onEnter() may return false but it does not need rollback. So a new out parameter is added to onEnter.
bool TxChangeCycleFsm::setState(TxChangeCycleState *newState, bool *pResult)
{
bool rollback, result;
TxChangeCycleState *oldState;
m_state->onExit();
oldState = m_state;
m_state = newState;
TRACE_OBJ(1, BRC_TX, STR("Change cycle state from %s to %s", oldState->getState().toString().c_str(), newState->getState().toString().c_str()));
result = m_state->onEnter(rollback);
if (pResult)
{
*pResult = result;
}
if (rollback)
{
m_state = oldState;
TRACE_ERROR(STR("Fail in onEnter of %s, rollback to %s", newState->getState().toString().c_str(), oldState->getState().toString().c_str()));
return false;
}
return true;
}

## Slide 200: Design suggestions
Putting functions into change cycle states is more preferred compared to put them into FSM or helpers.
Stateless functions (i.e. functions which have no relation with change cycle states) should be put into helpers if possible.
Helpers of FSM (e.g. TxChangeCycleBasicHelper, TxChangeCycleHelper or new helpers) should depend on different services if possible.
New helper should be created if there is a group of new functions with strong cohesion is needed in the FSM.

## Slide 201: Input
“TX Branch Control Restructuring A1.pptx”
Reason of change
  The class of TxBranchCtrl is too big. (~8000 lines, 265 member functions and 80 private members)
  Change cycle states are checked on a “need” basis via if statements. State pattern is wanted to improve code structure.

## Slide 202: RESOURCE HANDLER
SW location: ../app/sw/tx/serviceControl/resourceHandler
There is one instance of Resource Handler per Tx Module
Passive object
Modeled as a shared database that can be accessed by all services/service controllers in the Tx Module.
RH is a repository of the following information:
  FBS configuration and state data
  current HW configuration and state data for TxLo Freq, Power Level, TorLo
All services have access to this information.
Only Tx Branch Control can update this data

## Slide 203: RESOURCE HANDLER (CONTINUED)
Allocates resources upon requests from TxBranchCtrl (due to Set-up Requests).
Cleans up resources upon requests from TxBranchCtrl (due to Release Requests)
All services (except the TxCoordinationService) have access to RH via means of reference passed to them during initialization when dependencies are created

## Slide 204: RESOURCE HANDLER

## Slide 205: FBS DATA RECORD
Resource Handler stores the following configuration data for each FBS/FB:
  Filter Branch list
  Frequency data:
    frequency
    arfcn data
  Power data:
    carrier Power
    reserved Power
  Bandwidth data
    signal BW related
  Common data (per each entry):
    FBS Id or FB Id
    state
    RAT type
    carrier id (needed for FreqHop)
    Frequency configuration change status: changed/unchanged
    Power configuration change status: changed/unchanged
    State change status: changed/unchanged

## Slide 206: FBS/FB STATE TRANSITIONS
Similar to current carrier states and their transitions
FBS state is updated according to the event received as per the state transition diagram above
Filter Branch (FB) inherits its state from its parent FBS
setup
disabled
releasing
enabled
carrier
enabled
event
carrier
released
event
carrier
disabled
event
unallocated
carrier
setup
event
carrier frequency modify event
carrier power modify event
carrier
enabled
event
carrier
released
event
carrier power modify event
carrier frequency modify event
carrier
released
event

## Slide 207: FBS/FB STATES
unallocated – empty FBS record
setup – FBS resources and a unique FBS id was allocated due to a received carrier setup event
enabled – FBS has baseband traffic flowing
disabled – FBS is configured but baseband traffic is blocked (0-insertion is applied)
releasing - FBS is in the process of releasing; baseband traffic is blocked (0-insertion is applied)

## Slide 208: DATA RETRIEVAL FROM RESOURCE HANDLER
Data “pull” model is used
Services retrieve relevant FBS/FB or HW configuration data from Resource Handler on demand
TxBranchCtrl does not push data to Services (unless there is a scenario where it is absolutely needed)
Resource Handler provides a set of well defined interfaces for Services to access relevant data:
  Per Filter Branch Set data – returns vector of Freq/Power/BW data + Common data per Filter Branch Set
    getFrequencyData_allFBS()
    getPowerData_allFBS()
    getBandwidthData_allFBS()
    …
  Per Filter Branch data - returns vector of Freq/Power/BW data + Common data per Filter Branch
    getFrequencyData_allFB()
    getPowerData_allFB()
    getBandwidthData_allFB()
    …
  Notes:
  _allFB means all configured Filter Branches
  _allFBS means all configured Filter Branch Sets

## Slide 209: RESOURCE HANDLER – FBS CONFIGURATION
FBS configuration resides in two almost identical data bases in the Resource Handler:
  Committed Data DB
  Buffered Data DB
Committed Data contains FBS configuration records committed to the currently running cycle of frequency and power change.
Once the frequency change and power change cycle starts this data is locked- it is not updated throughout the cycle
Buffered Data contains FBS configuration records which are updated as new carrier events are arriving during the frequency and power change cycle

## Slide 210: FILTER BRANCH
FB state inherited from FBS
FCC : Frequency Configuration Change status
PCC : Power Configuration Change status
ZIns : Zero insertion flag (not covered in the rest of this discussion)
Enum values for FCC and PCC
  U: Unchanged
  C: Changed

## Slide 211: BUFFERED DATA UPDATE
TxBranchCtrl updates the Buffered data each time a carrier event arrives (set-up req, activate req, deactivate req, release req, freq modify req, power modify req)
Information updated in the Buffered data is per Filter Branch Set (a.k.a. carrier)
The following information is updated:
  final state of the FBS at the end of the cycle for which this Buffered entry will be committed
  Cycle Request pending flag
  configuration data if required

## Slide 212: CYCLE TRIGGERS
Cycle is triggered any if of the following occurs:
  Activate req received for any FBS
  Deactivate req received for any FBS
  Release req received for existing 1 FBS
  FBS is enabled and Frequency Modify req is received
  FBS is enabled and Power Modify req is received
1 If FBS is already in Committed data then it is called “existing”. For FBS which are “Newly created” in the Buffered data and a Release Req is received, no cycle is required – the FBS is just cleaned-up and the state is set to Unallocated.
No cycle is not triggered for the following events:
  FBS is disabled and Frequency Modify req received
  FBS is disabled and Power Modify req is received
  FBS is unallocated and Set-up req received
TxBranchCtrl determines if cycle needs to be triggered at the end of the current cycle
Steps:
  For each carrier in the Buffered Data
    if Cycle Needed == TRUE
      request cycle from TCS
      exit iteration

## Slide 213: COMMITTED DATA UPDATE
At the beginning of each cycle, TxBranchCtrl determines the changes to the Committed data.
TxBranchCtrl compares the Committed data and Buffered data from the previous cycle and determines the new set of Committed data.
RH is asked to store the new Committed data.
Common working data from the previous cycle (TxLo Freq, Power Level, TorLo, etc) is carried on to the next cycle.

## Slide 214: COMMIT
Commit observes the following steps:
  Remove all FBS that are in Releasing state in the Committed data
  Calculate Filter Branch configuration change status based on FBS state in Committed and Buffered data
  Update Committed Configuration Data (this is expected to be a simple copy of the pre-processed buffered configuration data).
  Reset the “newly created” flag for all FBS moving to Committed Data

## Slide 215: SPLC

## Slide 216: Questions / feedbacks
Now, I hope you are not afraid to have a look at the picture below   
From the most important DS for SPLC, TX Branch Control

## Slide 217: Power Level Change Introduction
This is introduction material with main focus on Radio Functions at Power Level Change which is the most complicated part of WP1186.
This material aims to help the reading/understanding of related DS:es and WP1186 implementation.
This material is NOT any kind of formal desigen specification.
It does NOT necessarily to be aligned exactly with DS:es or SW implementation since they keep on changing.
Expectation after this Presentation: SPLC(Seamless Power Level Change) is not so complicated as it was believed.

## Slide 218: Part 1 Radio Function View:What is PowerClass
40W
20W
Vdd
Biasing
TxStepATT
Vdd
Power
Biasing
Power
TxStepAtt
(Gain)
Power
PowerClass: Production calibrated PA configuration for certain power.
PowerClass: A better name could be PA size or Power Level
PowerClass/PowerLevel change (Legacy): from one production calibrated PA configuration to another production calibrated PA configuration.

## Slide 219: Part 1 Radio Function View:DL Gain Control Complete Pictures
Inside Warp
TOR Block
DPD Block
PA Block
Digital Domain
Analog Domain
40W
20W
TxStepAtt
(Gain)
Power
Biasing
Power
Vdd
Power
PA0
(existing
enabled cr)
Power
Tor
(Gain, Total)
Power
Blocking (Zero Insertion)
Why: avoid abrupt change at PA.
Where: before channel filter.
Most dangerous during PLC: TxStepAtt.

## Slide 220: Part 1 Radio Function View:LPLC (Legacy/Static Power Level Change)
Inside Warp
TOR Block
DPD Block
PA Block
Digital Domain
Analog Domain
40W
20W
TxStepAtt
(Gain)
Power
Biasing
Power
Vdd
Power
PA0
(existing
enabled cr)
Power
Tor
(Gain, Total)
Power
Problems with LPLC:
Long traffic interrupt, up to 1,6 seconds
Then RU can’t change PL very often. This introduced many complex rules with DS PowerClass.
Step 1: Blocking
Step 2: TxL::stop(), why ???
Step 5: TxL::start()
For new PL, it takes time !!!
Step 3: PA OFF,
reconfigure PA to next PL,
PA ON
Step 4: remove blocking
Performance problems with LPLC: DPD and Power efficiency for instance
Background Noise
Traffic situations with Carriers with very low power(s) -->
High PL (Analog Gain), very low PA0 (Digital Gain)
DPD performance !!!
Step 6: Finalizing. All function blocks which have dependency on PL:
PA0, MPL, CFR and DlPerf.
Power saving

## Slide 221: Part 1 Radio Function View: What is SPLC (Seamless Power Level Change)
Inside Warp
TOR Block
DPD Block
PA Block
Digital Domain
Analog Domain
20W
TxStepAtt
(Gain)
Power
Biasing
Power
Vdd
Power
PA0
(existing
enabled cr)
Power
40W
Tor
(Gain, Total)
Power
Goal for SPLC:
Shorter traffic interrupts
LPLC stops DPD
SPLC needs to keep DPD in tuned state
How ???
Set power level close to total setup power but with good margin for better performance
These power levels are not necessarily a production calibrated PC
Many interrupts of traffic,
which is not allowed by RS

## Slide 222: Part 1 Radio Function View: How to achieve a SPLC
Inside Warp
TOR Block
DPD Block
PA Block
Digital Domain
Analog Domain
Biasing
time
PA0
(existing
enabled cr)
time
Tor
(Gain, Total)
time
Phase 1(TxModuleSet):
Step 2: Blocking
Phase 1(TxModuleSet):
Step 1: TxL::pause(enable)
Pause DPD instead of stop()
Vdd
Phase 1(TxModuleSet):
Step 3: change TxStepATT
And PostDpd Gain together
40W
20W
TxStepAtt
(Gain)
time
Post DPD
Gain
What has be achived ???
Changed TxStepAtt with one shot !
Has pre-PA gain (Warp-to-PA) changed ???
Phase 1(TxModuleSet):
Step 4: TxL::pause(disable)
Resume DPD in Tuned state.
Phase 1(TxModuleSet):
Step 5: remove blocking
Phase 1: TxModuleSet
Phase 2: Scaling
PostDpdGain adjustment affects pre-PA gain
in the same way as TxStepAtt steps
One iteration of scaling cycle completed !
Not necessarily must be a
production calibrated PL!
Finalizing. All function blocks which have dependency on PL:
MPL, PA0, CFR and DlPerf.
Phase 3: Finalizing
TxL::recalibate()
PostDpd Adjustment for example:
Preparation: Inform TxL about the adjustments caused by TxStepAtt, TxL::initSPLC(U32 nIterations, float postDpdGainDiff_dB), TxL builds up adjustment for each iterations.
Step2 execution: Order TxL to perform an adjustment for a iteration TxL::setSPLCPostDpdGain(void).
Spreaded calculation/decisions among services based on total adjustment and nof iterations: Preparation and Execution
When decreasing Power
Reversed order with
Phase 1 and Phase 2.

## Slide 223: Part 1 Radio Function View: TxLO Moving
freq
Branch A
freq
Branch B
This slide is needed to explain the whole blocking scenario
FNCO2

## Slide 224: Part 1 Radio Function View: Traffic Blocking with Power Increasing
time
TxLo change preparation: Frequency calculation
Carrier Activation
Change TxLo
Update NCO and FreqHop LUT
Blocking: Zero insertion
SW Impl. Frequency Cycle
Change TxStepAtt
Scaling
UP!!!
Power Level
deblocking: remove zero insertion
SW Impl. Power Cycle
< 60 ms !!!
< 60 ms !!!
> 500 ms between blockings !!!
Blocking: Zero insertion
deblocking: remove zero insertion
TxL recalibration
> 500 ms
< 60 ms !!!
> 500 ms
Next Blocking
Training Signals interrupt traffic
Blocking: Zero insertion
”Should be” Scenario according to current requirement

## Slide 225: Part 1 Radio Function View: Traffic Blocking with only TxLO moving
time
TxLo change preparation: Frequency calculation
Frequency Modification
Change TxLo
Update NCO and FreqHop LUT
Blocking: Zero insertion
SW Impl. Frequency Cycle
< 60 ms !!!
> 500 ms between blockings !!!
deblocking: remove zero insertion
TxL recalibration
< 60 ms !!!
> 500 ms
Next move of TxLo, TxStepAtt
Training Signals interrupt traffic
Blocking: Zero insertion

## Slide 226: Part 2 SW View:Service Mapping
With current WP1186 implementation, the most important services are:
TxBranchCtrlSrv and PaSrv
SW elements
Radio Function blocks, DS.es

## Slide 227: Part 2 SW View: Class Overview
Tx-Module
Branch B (if exists)
Branch A
Func
layer
TxAdapter
CarrierListHandler
TxBranch
Repository
TxBranchCtrl
ResourceHandler
TxCoordination
CFR
FreqHop
MPL
NCO
PA0
PA1
PA (Branch)
TorLo
TxLo
TXL
TxStepAttenuator
TxBranchCtrl
PA (Shared VDD)
HALI1
Driver
Driver
Driver
Driver
Driver
Driver
Driver
Driver
Driver
(Services)
TorLo Synth
TxLo Synth
CarrierSubscriberIf

## Slide 228: Part 2 SW View:State Machines
The state machine of TxBranchCtrl

## Slide 229: Part 2 SW View:State Machines
The state machine of PaSrv

## Slide 230: Part 2 SW View: TxBranchCtrlSrv and PaSrv interactions
void PaSrv::notifyResultToClients( bool p_result )
{
TRACE_OBJ(9, PA, STR("notifyResultToClients, m_txBranchId=%d, p_result=%d.",
m_txBranchId, p_result ));
// Notify outstanding callback functions of the failure.
map<TxBranchEnumType, PaSrvClientRecord_t*>::iterator it;
for(it = m_paSrvClients.begin(); it != m_paSrvClients.end(); ++it)
{
switch(m_paSrvClients[(*it).first]->event)
{
case PA_SRV_EVENT_STATIC_PC_APPLY:
m_paSrvClients[(*it).first]->onStaticPowerChangePrepare.emit(p_result);
break;
case PA_SRV_EVENT_STATIC_PC_PREPARE_DONE:
m_paSrvClients[(*it).first]->onStaticPowerChangeBegin.emit(p_result);
break;
case PA_SRV_EVENT_STATIC_PC_BEGIN_DONE:
m_paSrvClients[(*it).first]->onStaticPowerChange.emit(p_result);
break;
case PA_SRV_EVENT_STATIC_PC_DONE:
m_paSrvClients[(*it).first]->onStaticPowerChangeComplete.emit(p_result);
break;
case PA_SRV_EVENT_DYNAMIC_PC_APPLY:
m_paSrvClients[(*it).first]->onDynamicPowerChangePrepare.emit(p_result);
break;
case PA_SRV_EVENT_DYNAMIC_PC_PREPARE_DONE:
m_paSrvClients[(*it).first]->onDynamicPowerChange.emit(p_result);
break;
case PA_SRV_EVENT_DYNAMIC_PC_DONE:
{
DynamicPowerStepChgResults_t results( p_result, m_currStepNum );
m_paSrvClients[(*it).first]->onDynamicPowerStepChange.emit(results);
break;
}
m_paSrvIf->staticPowerChangeApply(m_txBranchId))
TxBranchCtrl
bool TxBranchCtrl::doStaticPowerChangePrepare(void)
{
if ((m_paSrvIf->staticPowerChangePrepareDone(m_txBranchId)) == false)
return true;
}

## Slide 231: Part 2 SW View:Analysis of traces
/// from 0W ---> 40W
[1970-01-01 00:01:22.772] PaSrvA paSrvBranch.cc:354 TRACE2:PaSrvA doPowerLevelCalculation, branch=0 isPwrChgRequired=1 powerChgMode=0 currPLDbm=0 curPLWatt=0W, targetPLDbm=4600 targetPLWatt=40W numSteps=1
[1970-01-01 00:01:22.772] PaSrvA txBranchCtrl.cc:2223 TRACE1:onCalculateIsPowerChangeRequiredResponse: branch:0
[1970-01-01 00:01:22.772] TxBranchCtrlA txBranchCtrl.cc:2236 INFO:doCalculateIsPowerChangeRequiredResponse: returnStatus: 0, isPwrChgReq: 1, powerChgMode: 0, currentPowerLevel: 0, targetPowerLevel: 4600, numSteps: 1
/// @ PaSrv: PA_SRV_EVENT_STATIC_PC_APPLY
[1970-01-01 00:01:22.776] TxBranchCtrlA paSrv.cc:418 TRACE9:PaSrvA staticPowerChangeApply, p_branchId=0
[1970-01-01 00:01:22.776] PaSrvA paSrv.cc:1065 TRACE9:doPowerChangePrepare, client=0 m_paSrvState=0 event=2
[1970-01-01 00:01:22.776] PaSrvA paSrv.cc:835 TRACE9:validateEventAndClient, p_clientId=0 p_event=2 m_paSrvState=0
[1970-01-01 00:01:22.776] PaSrvA paSrv.cc:1807 TRACE9:notifyResultToClients, m_txBranchId=0, p_result=1.
// @ TxBranchCtrl: Preparing ....
[1970-01-01 00:01:22.776] PaSrvA txBranchCtrl.cc:1925 TRACE1:onStaticPowerChangePrepare: branch:0
[1970-01-01 00:01:22.776] PaSrvA txBranchCtrl.cc:2658 INFO:Branch: 0 States: TX/MODES/CHANGE_CYCLE: INACTIVE/TRAFFIC_BLOCK_PREPARATION/POWER_CHANGE
[1970-01-01 00:01:22.776] TxBranchCtrlA txBranchCtrl.cc:1978 TRACE1:doStaticPowerChangePrepare
/// @ PaSrv: PA_SRV_EVENT_STATIC_PC_PREPARE_DONE
[1970-01-01 00:01:22.776] TxBranchCtrlA paSrv.cc:435 TRACE9:PaSrvA staticPowerChangePrepareDone, p_branchId=0
[1970-01-01 00:01:22.776] PaSrvA paSrv.cc:1130 TRACE2:processing completed for client=0, m_paSrvState=2 event=2
[1970-01-01 00:01:22.776] PaSrvA paSrv.cc:1807 TRACE9:notifyResultToClients, m_txBranchId=0, p_result=1.
[1970-01-01 00:01:22.776] PaSrvA txBranchCtrl.cc:1934 TRACE1:onStaticPowerChangeBegin: branch:0
// @ TxBranchCtrl: Begining ......
[1970-01-01 00:01:22.776] TxBranchCtrlA txBranchCtrl.cc:2003 TRACE1:doStaticPowerChangeBegin
[1970-01-01 00:01:22.776] TxBranchCtrlA txStepAttSrv.cc:570 TRACE9: -- branch: 0, targetPowerLevel: 40.
[1970-01-01 00:01:22.776] TxBranchCtrlA txStepAttSrv.cc:447 TRACE2: -- Step Att frequency table are available.
/// @ PaSrv: PA_SRV_EVENT_STATIC_PC_BEGIN_DONE
[1970-01-01 00:01:22.776] TxBranchCtrlA txBranchCtrl.cc:2658 INFO:Branch: 0 States: TX/MODES/CHANGE_CYCLE: INACTIVE/TRAFFIC_BLOCKED/POWER_CHANGE
[1970-01-01 00:01:22.776] TxBranchCtrlA txBranchCtrl.cc:2020 TRACE1:Blocked traffic on activated carriers
[1970-01-01 00:01:22.776] TxBranchCtrlA paSrv.cc:449 TRACE9:PaSrvA staticPowerChangeBeginDone, p_branchId=0
[1970-01-01 00:01:22.776] PaSrvA paSrv.cc:1807 TRACE9:notifyResultToClients, m_txBranchId=0, p_result=1.
[1970-01-01 00:01:22.776] PaSrvA txBranchCtrl.cc:1945 TRACE1:onStaticPowerChange: branch:0
[1970-01-01 00:01:22.776] TxBranchCtrlA txBranchCtrl.cc:2032 TRACE1:doStaticPowerChange

## Slide 232: Part 3 Manual Test: RU Shell Commands
Inside Warp
TOR Block
DPD Block
PA Block
Digital Domain
Analog Domain
db list /pa/supportedPwrClass
100W 80W 60W 40W
$ db list */pa/Vdd/target
0x7521, 0x6D6C, 0x6565, 0x55DA
$ pa read volt
Vdd: 21994 (----)
/hw/txA/60W/mainStepAtt/freqTab
/hw/txA/60W/peakStepAtt/freqTab
/hw/txA/40W/mainStepAtt/freqTab P U32
0x000E4E1C, 0x0000000F, 0x000E6208, 0x0000000F,
0x000E7590, 0x0000000F, 0x000E8918, 0x0000000F,
0x000E9CA0, 0x0000000F
/hw/txA/60W/mainStepAtt/freqTab P U32
0x000E4E1C, 0x00000014, 0x000E6208, 0x00000014,
0x000E7590, 0x00000013, 0x000E8918, 0x00000013,
0x000E9CA0, 0x00000013
pa read paStepAttMain
pa read paStepAttPeak
(40W)
paStepAttMain: 16 (----)
//pa/txA/GMpa0/offset E S16
28, 41, 50, 64
/pa/txA/GMpa1/offset E S16
29, 38, 48, 62
/pa/txA/GDpa0/offset E S16
54, 59, 109, 209
/pa/txA/GMpa2/offset E S16
-92, -74, -73, -75
/pa/txA/GDpa1/offset E S16
94, 109, 159, 257
40 W
-----------
$ $ pa read bias
GMpa0: 3155 (----)
GMpa1: 3153 (----)
GMpa2: 2109 (----)
GMpa3: 2125 (----)
GDpa0: 3209 (----)
GDpa1: 3257 (----)
GDpa2: 3257 (----)
GDpa3: 3409 (----)
Tx Gain Doppio
-------------------------------
$ trx status
Branch A
DPD
{ subbandFiltSetup : 0x0000,
txAtt : 1957, txAttPeak : 1982,
torGain (torStepAtt+ tempCorTab + freqCorTab)
------------------------------------------------------------------
/tor/40W/stepCorTab
/tor/40W/freqCorTab
/hw/50x/BandVIII/tor/tempCorTab
$ trx torComp status
Tor Compensation is ON
torTemperature: 413, txSynthFreq: 940000(kHz)
gainCorr: 49707(0xC22B), (tempCorr: 6, freqCorr: 958, stepAttCorr: 0)
stepsLevelNow: 0, stepsToBeDone: 0
Tor step attenuator is enabled.
No command available,
There are traces:
txlProcBranchA iqController.cc:344 INFO:SPLC_TXL ===> IQHW[m0i(0x0000d683) m0q(0x0000d849)
warpA r DL_PA0_C0_ADJ
warp3 r DL_FB_B3_GA_CFG_MULT

## Slide 233: Part 3 Manual Test: New Commands Introduced by WP1186
$ txm help
txm help
Command syntax:
txm help [-l]
txm lssrvids
txm lssrvvar
txm brc {<variant> | all} {dump | lsparam | inj-setup | inj-activate <act/pm> <carrierId>}
txm brc {<variant> | all} get <param>
txm brc {<variant> | all} set <param> <value>
txm brc {<variant> | all} get-rh-committed-data
txm brc {<variant> | all} get-rh-buffered-data
txm brc {<variant> | all} get-zi-blocking-state-data
txm brc {<variant> | all} set-zi-perm-block
txm tcs dump
txm mpl {<variant> | all} dump
txm fhp {<variant> | all} dump
txm pa0 {<variant> | all} dump
txm pa1 {<variant> | all} dump
txm cfr {<variant> | all} dump
txm nco {<variant> | all} dump
txm txl {<variant> | all} dump
txm txl {<variant> | all} torlo move <freq_kHz>
txm txl {<variant> | all} torlo restore
txm txl {<variant> | all} event started
txm txl {<variant> | all} fault {lin | hw | ext} {raise | cease}
txm sta {<variant> | all} dump
txm pa {<variant> | all} dump
txm pa {<variant> | all} on
txm pa {<variant> | all} off
txm pa {<variant> | all} pl dump
txm pa {<variant> | all} blockid
txm pa {<variant> | all} idleCurr
txm pa {<variant> | all} scaling
txm tor dump
txm tlo dump
txm rh {<variant> | all} {buf | com | wrk | all} dump
One example:
$ txm pa0 all dump
SrvObj: Pa0SrvA
Latest Pa0 info on TX branch A
-------------------------------
DB carrierComp : 0
pSum : 0
pSumComp : 0
pSumMax : 0
pSumPos : 0
pSumCompPos : 0
pSumCompNeg : 0
K Factor : 0.000000
CTor : 0.000000
torGain : 0.000000
fMidAmplitude : 0.000000
dlPowerCompLimit : 0
cxComp[0] : 0.000000
getFcompPa0[0] : 0.000000
fbId: 3, targetDlPa0Adj = 28540 = 0x6f7c
SPLC vector values:
Number of steps: 0
-------------------------------
SrvObj: Pa0SrvB
Latest Pa0 info on TX branch B
-------------------------------
DB carrierComp : 0
pSum : 0
pSumComp : 0
pSumMax : 0
pSumPos : 0
pSumCompPos : 0
pSumCompNeg : 0
K Factor : 0.000000
CTor : 0.000000
torGain : 0.000000
fMidAmplitude : 0.000000
dlPowerCompLimit : 0
SPLC vector values:
Number of steps: 0
-------------------------------

## Slide 234: Part 4: SPLC Trouble-shooting 1
Prerequisite:
A known working SW LMC for LPLC
Basic idea:
Take advantage of one special rule of LPLC: ONE LTE carrier, PA is configured to the nearest higher PC.
Create two carrier configurations with LPLC and SPLC respectively, which have the same power setting
in both Digital and Analog domain as those of LPLC.
2. Read gain settings from LPLC and SPLC carriers respectively.
3. Compare the results to isolate where the problem arise.
Step1: Test with LPLC LMC,
Change database, set …/seamlessPowerLevelEnable to false. setup and activate one LTE carrier with power set to 21W (bigger than 20W).
Read all gain setting described in the previous slide.
Details actions (take a RU with 20W and 40W PC for example):
Step2: Test with SPLC LMC,
Change database, set …/seamlessPowerLevelEnable true again. setup and activate two LTE carriers with power set to 20W.
Read all gain setting described in the previous slide.
Step3: Compare two results to identify where is the major difference(s)
At the first days after SPLC delivery, there
might be such a situation that there is no known
working LMC on a certain type of RU.
It could also be helpful with other fast fault
identifications
Due to performance drawback of SPLC, some database parameters are to be introduced, like…/PaPowerLevelMargin
It means that step2 needs to be adjusted according to these new margins, for instance 20W + 20W –PaPowerLevelMargin)
The basic idea to create two comparable gain settings should still work.

## Slide 235: Rx Module

## Slide 236: Architectural requirements
The RX module shall be scalable on RX antenna branches.
The RX module shall be able to handle concurrent calls to the RX module from higher layers, i.e. CarrierList events.
The RX Branch Controller shall handle shared resources between RX antenna branches, i.e. shared synths like RX LO, without risk for deadlock.
Differences compared to the TX module:
There are no long-running tasks with long waiting in the UL functionality. The TX module needs to handle SPLC and TX linearization.
The number of change cycles that defines an order in which all antenna branches that shares resources must follow synchronized is lower. In the TX module there is frequency and power change.

## Slide 237: Architectural design rules
All communication with the RX module goes via the RX Module Interface package.
There is no dependency from the RX module to the layers above.
The RX module depends on the layers below, but not vice versa.
A higher level package in the RX module above may depend on a lower level package in the RX module, but not vice versa.
The only dependency from the RX module to the DriverInterface is that the services use the DriverInterface. No other RX package uses the DriverInterface.
The only dependency towards the RX Services package is that the RX Control package uses the services via their interface classes. The controllers have no dependency to the concrete service implementations.
Each service is a separate package inside the RX Services package. There are no dependencies between the services.
The services depend on the RX Service Common package. The RX Service Common package does not use any RX package apart from the RX Common package.
Link

## Slide 238: RX Module SW Architecture
Link
RX Broker package
  A temporarily introduced layer between the CarrierResourceHandler and the RX Module.
RX Startup package
  Starts up the RX module by parsing the database file serviceSets.txt and instantiating controllers and services.
RX Module Interface package
  The interface to the RX module.
RX Control package
  The branch controller and the sub-controllers.
RX Services package
  RX services.
RX Service Common package
  Common RX service functionality used by the services in the RX module.
RX Common package
  Common RX module functionality used by the other packages in the RX module.

## Slide 239: RX Module Packages
Link

## Slide 240: Scaling – RX Module example
Rx branch controller models HW branch utilizing services
Scaling by instances
’Automatically’
’Infinite’
Rx branch ctrl A
Rx branch ctrl B
Rx branch ctrl C
Rx branch ctrl D
How?
instantiated

## Slide 241: Shared HW, RX module example
How to do when HW is not owned by single branch?

## Slide 242: Change cycle, RX Module example
Cycle is a sequence of operations required for shared HW change
  E.g. Frequency Change Cycle (LO’s)

## Slide 243: RX/UL Module functionalities
The RX module encapsulates the following functionalities:
  Time alignment
  Equalizer
  Frequency hopping
  Subband
  Frequency configuration
  Filter
  Interference measurement
  Supervision
  Analog configuration and control
  Clock control
  Gain

## Slide 244: Simple Example, startup, rx module

## Slide 245: Simple Example, startup, rx branch ctrl

## Slide 246: Simple Example, carrier setup

## Slide 247: UT

## Slide 248: SW HIGH LEVEL VIEW
Reside in the main application directory (sw/app)
Comply with Radio SW directory structure and naming convention (if, inc, src, unitTest, Makfiles, etc…)
Service directory naming convention <service name abbreviation>Service (e.g. mplService)
Unit Test stubs contains a mix of Google Mock stub methods
Mock stubs file names starts with the word mock (e.g. mockBbDataSrv)
doc sub-directory is not used any longer. It is replaced by directory radiosw/sw/app/doxygen/
Code walkthrough…
Notes: TxBranchCtrl: the main controller for a Tx Branch.
TxBrFaultAdvisor: works with Tx Branch Controller and the Fault Manger (FM) at the Resource layer for recovery and reporting of faults reported by Txl or supervision processes.
TxPowerSupCtrl: sub-controller of Tx Branch Controller, supervise tx and tor power from Pa1Srv and TxlSrv to detect sleeping cell.
Tx Timing Phase Controller: the main controller for timing related operations, for instance, time alignment, subband phase compensation, freqHop time offset, etc..
LimitSlotMeasControl
TxPowerSaveCtrl
The following SW components in the Service layer of Tx Module manage one or more hardware blocks in the radio TX HW chain:
TorLoSrv: manages the shared TOR LO component.
TxLoSrv: manages the shared TX LO HW component.
TxlSrv: interacts with the Txl SW to configure the PA observation loop (also known as gain control loop). The components participating in the PA observation loop are DPD FPGA, VGA and TOR Step attenuator blocks.
PaSrv: manages the analog PA HW component.
Pa0Srv: manages the filter branches of the digital ASIC PA0 HW block.
Pa1Srv: manages the digital ASIC PA1 HW block for each TX branch.
TxStepAttSrv: manages the analog step attenuator before the PA.
NcoSrv: manages the filter branches of the digital ASIC NCO block.
MplSrv: manages the filter branches on the digital ASIC Mean Power Limiter (MPL) HW block.
FreqHopSrv: manages the filter branches on the digital ASIC Frequency Hop HW block.
CfrSrv: manages the digital ASIC clipping (crest factor) HW block.
ChannelFilterSrv : manages the filter branches on digital ASIC channel filter HW block.
PaComp: controls the PA compensation.
BbDataSrv: manages the CPRI to Gamma block.
SbpsSrv: configures DPD FPGA expansion interface registers.
BfnAdvanceSrv: configure BFN_ADVANCE registers.
FineDelaySrv: configure delay registers in filter branches.
PaBranchDelaySrv: configure delay registers in PA branches, and introduced for the WARP3.x digital ASIC based radio and newer chips as long as the delay in PA branch (MCB part in Xenon) is configurable.
FreqHopTimeOffsetSrv: configure delay registers for frequency hopping functionality, and introduced for the WARP3.x digital ASIC based radio and newer chips as long as the delay in PA branch (MCB part in Xenon) is configurable.
PhaseCompSrv: configure phase compensation coefficients for LTE subband carriers or disable phase compensation for carriers of other types.
DigitalTorifSrv: configures digital ASIC TORIF HW block.
ZeroInsertService: performs 0-insertions.
DacSrv: configure the DAC (Digital to Analog Convertor) component in the Tx DL HW block chain.
OverTempSrv: generates analog and digital backoff requests according to temperature sensor readings

## Slide 249: How to secure legacy behavior
The new UT.
Legacy Mira and Terras case.
  No any change to Mira/Terras cases since no any function change in the restructuring
Move code with least change.

## Slide 250: What was done by Ligntnning
Add some UT cases to increase code coverage. (Gerrit)
Remove old UT. (Gerrit)

## Slide 251: Code: Unit Test
TEST(vddSupervision,checkHighVoltage)
{
RuError err;
MockInstanceToken instance(“A”);
MockVoltageSensor mockVdd(err,“Vdd”,instance);
ASSERT_EQ(false,err); // Shouldn’t fail unless error in test case (Vdd:A already added)
VddSupervision vddSupervision(instance);
vddSupervision.init(err);
EXPECT_FALSE(err);
EXPECT_CALL(mockVdd,read(_)).WillOnce(Return(32500*milliVolt));
EXPECT_EQ(false,vddSupervision.checkHighVoltage(err));
EXPECT_EQ(false,err);
EXPECT_CALL(mockVdd,read(_)).WillOnce(Return(32501*milliVolt));
EXPECT_EQ(true,vddSupervision.checkHighVoltage(err));
EXPECT_EQ(false,err);
}
Notes: ASSERT is used instead of EXPECT since testing MockVoltageSensor is not part of this test case (it’s already tested in the hali1 unit test). Creating a resource mock will fail if a mock with the same name and instance has already been added, so it does makes sense to check for an error, which would indicate a problem with the test case.
The underscore in read(_) is the AnythingMatcher which is used here to match any reference to an RuError.

## Slide 252: Code: Unit Test 2
TEST(vddSupervision,errorHandling)
{
RuError err;
MockInstanceToken instance(“A”);
MockVoltageSensor mockVdd(err,“Vdd”,instance);
ASSERT_EQ(false,err); // Shouldn’t fail unless error in test case (Vdd:A already added)
VddSupervision vddSupervision(instance);
vddSupervision.init(err);
EXPECT_FALSE(err);
// Test that when VoltageSensor::read fails, checkHighVoltage will propagate the error.
RuError readError(“Failed to read from device”);
EXPECT_CALL(mockVdd,read(_)).WillOnce(SetArgReferee<0>(readError));
vddSupervision.checkHighVoltage(err)); // No need to check return value
EXPECT_EQ(true,err);
}
Notes: This test case tests error handling in checkHighVoltage by making mockVdd.read() fail. It could be part on the test case on the previous slide, but has been separated here for PowerPoint reasons.
The first part of the test case (create mock, etc) is identical to the previous one.
When VoltageSensor::read sets the RuError the return value is not valid, so no return value is set in EXPECT_CALL. Here we assume that the same holds for checkHighVoltage, which is why we do not care about its return value. But that part is of course up to the Service designers.

## Slide 253: Previous training sessions
ETK training page:
https://ericoll.internal.ericsson.com/sites/ETK_Radio_SW_Core_Team/Documents/Forms/AllItems.aspx?RootFolder=%2Fsites%2FETK%5FRadio%5FSW%5FCore%5FTeam%2FDocuments%2FRadio%20SW%20training%20%28ETK%29%2FPresentations
Ericsson Play recordings:
  RBS introduction https://play.ericsson.net/media/t/0_8o9oytaf
  TX functions https://play.ericsson.net/media/t/0_pxkphfwy
  RX Functions https://play.ericsson.net/media/t/0_15tr4m95
  Radio Software https://play.ericsson.net/media/t/0_tj18rh3d

## Slide 254: Q&A